| Approved | By | Parameter | Info on Page | Limits | Value |
| --- | --- | --- | --- | --- | --- |
|  | HPS/ Steve Green | ADV1 Performance Assessment (change in tank pressure & propellant consumption, observed vs predicted) |  |  |  |
|  | FDG | ADV1 Performance Assessment (% hot/cold) |  |  |  |
|  | FDG | Current OD Uncertainty |  | Within ground station FOV for post spin-up passes |  |
|  | FDG | Target Orbit Period Uncertainty (Napoleon plot) |  | No >4h ecipses |  |
|  | FDG | No Additional Delta-V Burn Trajectory |  | Just for comparison |  |
|  | FDG | No ADV2 Burn Trajectories |  | Decide on backup plan |  |
|  | FDG | Helionose Progression |  | Clockwise |  |
|  | FDG | Apogee Radius |  | Always <= 55Re geoc. |  |
|  | FDG | Perigee Radius |  | Always >= 3Re geoc. |  |
|  | FDG | Quicklook Communications Analysis - only if there is a major difference in perigee profiles |  | Miss 3dB link margin for >1 perigee in a row for 10 years |  |
|  | FDG | Apogee & Perigee Times |  | N/A |  |
|  | FDG | Crossing Times |  | N/A |  |
|  | FDG | Viewperiods Report |  | Contacts Still Valid |  |
|  | MOC | SAP |  | Contacts Still Valid |  |
|  | MOC | USN Coverage for ADV2 |  | N/A |  |
|  | MOC | USN Coverage for ADV3 |  | Available at time of MAC |  |
|  | MOM | Time of ADV2 (6/16 1900 UTC) |  | In viable viewperiod |  |
|  | FDG | Duration of ADV2 Burn (600s) |  | 600s - no tolerance |  |
|  | MOM | Time of ADV3 (6/17 1100 UTC) |  | In viable viewperiod |  |
|  | FDG | Duration of ADV3 Burn ( s) |  | Up to 600s |  |
|  | MOC | ADV2 & ADV3 ATS |  | N/A |  |
|  | SYS, ACS, MOC, MOM, PM, ISOC, FDG | Approved ADV2 & ADV3 ATS (prior to MAC) |  | N/A |  |
|  | SYS, MOC, MOM, PM, ISOC, FDG | Approved Contact ATS (prior to MAC) |  | Command Limit Contraints not violated (<240 commands) |  |
|  | SYS | ACS TLM (from contact before MAC) |  | GREEN |  |
|  | SYS | HPS TLM (from contact before MAC) |  | GREEN |  |
|  | SYS | EPS TLM (from contact before MAC) |  | GREEN |  |
|  | SYS | SCB TLM (from contact before MAC) |  | GREEN |  |
|  | SYS | Temperature Plots |  |  |  |

S/C State as of pass prior to MAC:

Sun Angle Range ______    	Post-Maneuver Expected Sun Angle _______  tol +/- 1 degree (quaternions) - provide running plot of sun pointing angle

Spin Rate  ______		Post-Maneuver Expected Spin Rate _______   tol.  +/- 1 rpm

ADV1 Maneuver Success Criteria :

Correct Polarity				_______

Maneuver Completed at Specified Time	_______

End of burn pressure within limits		_______

Cat bed heaters 5N & 22N on & off	_______

Nutation damping pulses  		_______

Spin down pulses	  		_______

SCB State ______

CEU Mode ______

FC Mode  ______

ACE Mode ______

EPS Mode ______

Star Tracker ______

ACS Low Rate Sensor ______

Fuel used Table : Grey boxes do not have meaningful values - leave blank

| Immediately before/after maneuver | Tank 1 Pres (SYS) psi | Tank 1 Temp (SYS) °C | Tank 2 Pressure (SYS) psi | Tank 2 Temp (SYS) °C | Delta-V (FDG) m/s | Fuel Use (SYS, FDG, MT) kg | Fuel Remaining (SYS, FDG, MT) kg |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Est | Obs | Est | Obs | Est | Obs | Est | Obs | Est | Recon | OD | Recon | OD* | Est | Obs |
| Pre-Repointing |  | 173.43 |  | 18.82 |  | 173.14 |  | 20.05 |  |  |  |  |  |  | 16.41 |
| Post-Repointing | 173.43 |  | 18.82 |  | 173.14 |  | 20.05 |  |  |  |  | 0.004 |  | 16.41 |  |
| Pre-Spin Up | 173.43 |  | 18.82 |  | 173.14 |  | 20.05 |  |  |  |  |  |  | 16.41 |  |
| Post-Spin Up | 171.66 |  | 18.82 |  | 171.35 |  | 20.05 |  |  |  |  | 0.197 |  | 16.21 |  |
| Pre-ADV1 | 170.8 |  | 18.82 |  | 170.8 |  | 20.05 |  |  |  |  |  |  | 16.21 |  |
| Post-ADV1 | 140.28 |  | 18.82 |  | 140.28 |  | 20.05 |  | 103.1 |  |  | 4.17 |  | 12.04 |  |
| Pre-ADV2 | 140.28 |  | 18.82 |  | 140.28 |  | 20.05 |  |  |  |  |  |  | 12.04 |  |
| Post-ADV2 | 121.24 |  | 18.82 |  | 121.24 |  | 20.05 |  | 94.16 |  |  | 3.67 |  | 8.37 |  |
| Pre-ADV3 | 121.24 |  | 18.82 |  | 121.24 |  | 20.05 |  |  |  |  |  |  | 8.37 |  |
| Post-ADV3 | 111.0 |  | 18.82 |  | 111.0 |  | 20.05 |  | 67.62 |  |  | 2.52 |  | 5.85 |  |
| Pre-Spin Down | 111.0 |  | 18.82 |  | 111.0 |  | 20.05 |  |  |  |  |  |  | 5.85 |  |
| Post-Spin Down | 110.01 |  | 18.82 |  | 110.01 |  | 20.05 |  |  |  |  | 0.197 |  | 5.65 |  |
| Pre-Repointing | 110.01 |  | 18.82 |  | 110.01 |  | 20.05 |  |  |  |  |  |  | 5.65 |  |
| Post-Repointing | 110.0 |  | 18.82 |  | 110.0 |  | 20.05 |  |  |  |  | 0.006 |  | 5.65 |  |

* Minimal accuracy

Table Change History (date, person, change) :

Approvals By  :

_____ Dave McComas 		_____ Robert Lockwood		_____ John Carrico

_____ John Scherrer    		_____ Ryan Tyler		_____ Lisa Policastri

_____ Nathan Schwadron  	_____ Bret Hautamaki		_____ Ryan Lebois

_____ Chelle Reno		_____ Jim Bobbett		_____ Marissa Intelisano

_____ Mark Tapley		_____ Jeff Godward

_____ Tim Perry

_____ Sheral Wesley