IBEX Goat Herder  24 Dec 15

The PERIGEE contacts with USN were nominal for command/telemetry and the inertial maneuver successful.

The IBEX_Hi Sweep Table was successfully changed

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Wednesday, December 23, 	357	0800	USHI01	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	776	21 desc	64ksps	215

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

840	2	1434	32	0	0

VC 2 Write Pointer 	26409	VC 2 Write Pointer End	26508

VC 2 Read Pointer 	4910	VC 2 Read Pointer End	4910

Orbit# 310 IBEX_Hi Sweep Table Change contact

CAR# 776 IBEX_Hi Sweep Table Change

1.@CEU_MODE HVENG

2.@CEU_MODE HVSTANDBY

3.sweep_table_upload_150910.scr(table_hi_AllESA,quit)

4.@CEU_MODE HVENG

5.@CEU_MODE HVSCI

@FMI_SetDownlink(40k)

@FTG_DumpBackorbit (from start,0,0,0,0)

@ECT_SetRelay (stx,off)

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Thursday, December 24, 2015	358	1000	USHI01	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	777	11 asc	320ksps	214

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1541	1	0	0	0

VC 2 Write Pointer 	28648	VC 2 Write Pointer End	28695

VC 2 Read Pointer 	27977	VC 2 Read Pointer End	27977

Orbit# 310 Tracking Contact/reset_master_timer.scr

CAR# 777 Upload Orbit# 312 ATS  1.IBEX_2016_002_o0312a_v002.scr(507-611)

ops_set_sc_time.scr

@FTG_DumpBackorbit (from start.0.0.0.0)

@ECT_SetRelay (stx,off)

IBEX Orbit# 310 PERIGEE Target Vectors 24 Dec 15

J2000	Spin Axis

ECI X	0.046247

ECI Y	-0.916269

ECI Z	-0.397884

Precession Maneuver

MPS Diff	0.632	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	272.889	deg

Declination - DEC	-23.446	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	0.346	deg

0.07714090	ActNor.EstInrToBdy[0]

0.83246100	ActNor.EstInrToBdy[1]

-0.54310000	ActNor.EstInrToBdy[2]

0.07810430	ActNor.EstInrToBdy[3]

1134990000.000	ActNor.EstTime

MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	0.052071000

MPS Cmd Vector Y	-0.912217000

MPS Cmd Vector Z	-0.406386000

CSS Angle TLM	0.36948	23 Dec 15 @0800

CSS Sun-Pointing Angle	0.73896

CSS Angle TLM	0.540317	24 Dec 15 @1000

CSS Sun-Pointing Angle	1.080634

Pre-Burn

Thruster 1	3152	23 Dec 15 @0800

Thruster 2	3072

Thruster 3	3520

Thruster 4	3600

Post-Burn

Thruster 1	3296	24 Dec 15 @1000

Thruster 2	3216

Thruster 3	3696

Thruster 4	3776

Number of Pulses

Thruster 1	144

Thruster 2	144

Thruster 3	176

Thruster 4	176

Thruster Pairs

Thruster 1 & 2	288

Thruster 3 & 4	352