IBEX Goat Herder  2 Jan 16

The Perigee contacts for Orbit# 311 were nominal for command/telemetry and the inertial maneuver successful.

SSRdata blocks from Orbit# 310 that are currently in review were re-dumped successfully.

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Saturday, January 02, 2016	002	0430	USHI01	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	778	779	10 desc	64ksps

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1159	1	0	0	1230	0

VC 2 Write Pointer 	51271	VC 2 Write Pointer End	51311

VC 2 Read Pointer 	27977	VC 2 Read Pointer End	27977

Orbit# 311 Tracking Contact

reset_master_timer.scr

CAR# 779 Re-Dump Orbit# 310 Blocks  1.SSR_Dump.scr (start 4910,NUMBLKS  1230)

CAR# 778 Orbit# 312 IBEX_Hi Gain Test  1.IBEX_2016_002_o0312a_HGC_v001.scr (676-739)

ops_set_sc_time.scr

IBEX Orbit# 311 PERIGEE Target Vectors  2 Jan 16

J2000	Spin Axis

ECI X	0.205141

ECI Y	-0.898303

ECI Z	-0.388548

Precession Maneuver

MPS Diff	0.753	deg

*MPS Diff should be < 1.5*

0.56568600	ActNor.EstInrToBdy[0]

0.61177900	ActNor.EstInrToBdy[1]

-0.31220900	ActNor.EstInrToBdy[2]

0.45634600	ActNor.EstInrToBdy[3]

1135750000.000	ActNor.EstTime

Right Ascension - RA	282.864	deg

Declination - DEC	-22.864	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	0.575	deg

Orbit# 311 MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	0.212444000

MPS Cmd Vector Y	-0.892507000

MPS Cmd Vector Z	-0.397869000

CSS Angle TLM	0.991303	28 Dec 15 @1900

CSS Sun-Pointing Angle	1.982606

CSS Angle TLM	0.435662	02 Jan 16 @0430

CSS Sun-Pointing Angle	0.871324

Pre-Burn

Thruster 1	3712	28 Dec 15 @1900

Thruster 2	3632

Thruster 3	4144

Thruster 4	4224

Post-Burn

Thruster 1	3856	02 Jan 16 @0430

Thruster 2	3776

Thruster 3	4320

Thruster 4	4400

Number of Pulses

Thruster 1	144

Thruster 2	144

Thruster 3	176

Thruster 4	176

Thruster Pairs

Thruster 1 & 2	288

Thruster 3 & 4	352

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Saturday, January 02, 2016	002	1300	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	11 asc	320ksps	270 watts

EBNO Values	EBNO Values 3	AGC Strength

@1259=6.06-6.91db(320k)	@1259=-104.12db(320k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1734	1	1310	0	23669	0

VC 2 Write Pointer 	51645	VC 2 Write Pointer End	51687

VC 2 Read Pointer 	27977	VC 2 Read Pointer End	51646

Orbit# 311 SSR_Dump/Tracking Contact

SSR_Dump.scr (new

@FTG_DumpBackorbit (from start,0,0,0,0)

@ACT_ResetTaskRawFailed 	(AC_FDC)

@ECT_SetRelay (stx,off)