IBEX Goat Herder  11 Jan 16

The Perigee contacts for Orbit# 312 were nominal for command/telemetry and the inertial maneuvers successful.

The SSR_Data in Orbit# 309 was re-dumped successfully along with the Star Tracker Image

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Monday, January 11, 2016	011	0500	USHI01	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	781	9 desc	160ksps

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1913	1	0	0	21988	0

VC 2 Write Pointer 	8090	VC 2 Write Pointer End	8148

VC 2 Read Pointer 	51646	VC 2 Read Pointer End	8098

Orbit# 312 SSR_Dump/Tracking Contact

reset_master_timer.scr

SSR_Dump.scr (new)

CAR# 781 Upload Orbit# 314 ATS 1.IBEX_2016_020_o0314a_v001.scr (149-247)

@ACT_ResetTaskRawFailed (AC_FDC)

IBEX Orbit# 312 PERIGEE Target Vectors  11 Jan 16

J2000	Spin Axis

ECI X	0.365379

ECI Y	-0.816812

ECI Z	-0.446448

Precession Maneuver

MPS Diff	0.816	deg

*MPS Diff should be < 1.5*

0.16455200	ActNor.EstInrToBdy[0]

0.83435400	ActNor.EstInrToBdy[1]

-0.42959500	ActNor.EstInrToBdy[2]

0.30368400	ActNor.EstInrToBdy[3]

1136530000.000	ActNor.EstTime

Right Ascension - RA	294.100	deg

Declination - DEC	-26.516	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	4.973	deg

MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	0.357338000

MPS Cmd Vector Y	-0.814040000

MPS Cmd Vector Z	-0.457874000

CSS Angle TLM	1.1736	07 Jan 16 @1730

CSS Sun-Pointing Angle	2.3472

CSS Angle TLM	2.02456	11 Jan 16 @0500

CSS Sun-Pointing Angle	4.04912

Pre-Burn

Thruster 1	4288	07 Jan 16 @1730

Thruster 2	4208

Thruster 3	4752

Thruster 4	4832

Post-Burn

Thruster 1	4688	11 Jan 16 @0500

Thruster 2	4576

Thruster 3	5120

Thruster 4	5232

Number of Pulses

Thruster 1	400

Thruster 2	368

Thruster 3	368

Thruster 4	400

Thruster Pairs

Thruster 1 & 2	768

Thruster 3 & 4	768

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Monday, January 11, 2016	011	1300	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	782	783	11 asc	320ksps	327

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1907	1	0	0	23182	0

VC 2 Write Pointer 	8442	VC 2 Write Pointer End	8498

VC 2 Read Pointer 	8098	VC 2 Read Pointer End	8098

Orbit# 312 SSR_Dump/Tracking Contact

CAR# 782 Re_Dump Orbit# 309 SSR_ Blocks(start112800,NumBlks 18272) (start 0,NumBlks 	4910)

CAR# 783 Orbit# 312 Star Tracker Image Dump

@AHW_ReadSttlmAttitude

@AKT_ReadAkrTm

@AHW_ReadSttlmHK

@AHW_ReadSttlmFailure

ops_acs_tracker_image.scr (jpeg)

ops_acs_tracker_check_time.scr

ops_acs_tracker_check_hk.scr

ops_acs_tracker_centroids.scr

ops_acs_tracker_params_dump.scr

@AKT_WriteTlmDest (0,0)

@AHW_ReadSttlmAttitude

@AKT_ReadAkrTm

@AHW_ReadSttlmHK

@AHW_ReadSttlmFailure