IBEX Goat Herder  20 Jan 16

The Perigee contacts were nominal for command/telemetry and the inertial maneuver successful.

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Wednesday, January 20, 2016	020	1100	USAK

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	784	12 asc	320ksps	360 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1556	1	1309	0	0	0

VC 2 Write Pointer 	31087	VC 2 Write Pointer End	31134

VC 2 Read Pointer 	30546	VC 2 Read Pointer End	30546

Orbit# 313 SSR_Dump/Tracking Contact

reset_master_timer.scr

CAR# 784 Upload Orbit# 315 ATS  1.IBEX_2016_029_o0315a_v001.scr (353-457)

ops_set_sc_time.scr

@ACT_ResetTaskRawFailed(AC_FDC)

@FTG_DumpBackorbit(from start,0,0,0,0)

@ECT_SetRelay(stx, off)

IBEX Orbit# 313 PERIGEE Target Vectors 20 Jan 16

J2000	Spin Axis

ECI X	0.502908

ECI Y	-0.754297

ECI Z	-0.422042

Precession Maneuver

MPS Diff	0.571	deg

*MPS Diff should be < 1.5*

0.50874900	ActNor.EstInrToBdy[0]

-0.67245500	ActNor.EstInrToBdy[1]

0.53661200	ActNor.EstInrToBdy[2]

0.03204170	ActNor.EstInrToBdy[3]

1137330000.000	ActNor.EstTime

Right Ascension - RA	303.692	deg

Declination - DEC	-24.964	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	5.022	deg

IBEX Orbit# 313 MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	0.499151000

MPS Cmd Vector Y	-0.751795000

MPS Cmd Vector Z	-0.430873000

CSS Angle TLM	0.249446	15 Jan 16 @1900

CSS Sun-Pointing Angle	0.498892

CSS Angle TLM	1.87185	20 Jan 16 @1100

CSS Sun-Pointing Angle	3.7437

Pre-Burn

Thruster 1	4944	15 Jan 16 @1900

Thruster 2	4832

Thruster 3	5520

Thruster 4	5632

Post-Burn

Thruster 1	5456	20 Jan 16 @1100

Thruster 2	5344

Thruster 3	6048

Thruster 4	6160

Number of Pulses

Thruster 1	512

Thruster 2	512

Thruster 3	528

Thruster 4	528

Thruster Pairs

Thruster 1 & 2	1024

Thruster 3 & 4	1056