IBEX Goat Herder  30 Mar 16

The Apogee Contacts for Orbit# 321 were nominal for command/telemetry and the sun maneuver successful.

There were no valid quaternions from the star tracker after the software upload.

The following objectives were completed

- CAR# 815 New Star Tracker software upload

Ops_acs_tracker_TOPS_kernel_load_20160330.scr

@AHW_ReadSttlmAttitude

@ACT_TMSta

ops_acs_tracker_image.scr (uncompressed)

- CAR# 816 CSS_Telemetry/Set CEU default spin period css_telemetry_v002.scr

CEU_SET_PARAMETER (57268,124) @1931 UTC

The new CSS-based CEU default spin rate is 57268:

|  | Spin Rate | Spin Period | CEU Setting |
| --- | --- | --- | --- |
| CSS0 | 4.191329754 | 14.31526592 | 57261 |
| CSS1 | 4.189042764 | 14.32308128 | 57292 |
| CSS2 | 4.191329531 | 14.31526669 | 57261 |
| CSS3 | 4.191297481 | 14.31537615 | 57261 |
| Average | 4.190749882 | 14.31724751 | 57268 |

| CSS Angle TLM | 1.59385 |  |
| --- | --- | --- |
| CSS Sun-Pointing Angle | 3.1877 |  |
|  |  | 23 Mar 16 @1500 |
| CSS Angle TLM | 2.30444 |  |
| CSS Sun-Pointing Angle | 4.60888 |  |
|  |  | 30 Mar 16 @1949 |
| Pre-Burn |  |  |
| Thruster 1 | 9120 | 23 Mar 16 @1500 |
| Thruster 2 | 8864 |  |
| Thruster 3 | 11216 |  |
| Thruster 4 | 11472 |  |
| Post-Burn |  |  |
| Thruster 1 | 9360 | 30 Mar 16 @1949 |
| Thruster 2 | 9104 |  |
| Thruster 3 | 11600 |  |
| Thruster 4 | 11856 |  |
| Number of Pulses |  |  |
| Thruster 1 | 240 |  |
| Thruster 2 | 240 |  |
| Thruster 3 | 384 |  |
| Thruster 4 | 384 |  |
| Thruster Pairs |  |  |
| Thruster 1 & 2 | 480 |  |
| Thruster 3 & 4 | 768 |  |