IBEX Goat Herder  1 Apr 16

The Perigee Contacts for Orbit# 321 were nominal for command/telemetry and the sun maneuver successful.

The SSR dump was not complete. The remaining Blocks will be dump during Perigee of Orbit# 322

The following objectives were completed

- CAR# 818  Upload Orbit# 323 ATS

IBEX_2016_101_o0323a_Recovery_v001.scr (77-158)

- Reset_master_timer.scr

- SSR_Dump.scr (New) (32806 Blks, 5444 remaining Blks)

VC2= 27444 with 0 errors

- Read Telemetry Gatherer rates @FTG_ReadTGEntry

175  (15, 2, 300, 22)

176  (30, 4, 300, 24)

181  (30, 12, 180, 48)

200 (10, 1, 360, 23)

201  (10, 5, 360, 27)

206 (30, 19, 240, 43)

- CAR# 817   CSS_Telemetry/Set CEU default spin period css_telemetry_v002.scr

CEU_SET_PARAMETER (,124) @1931 UTC

The new CSS-based CEU default spin rate is :57433

|  | Spin Rate | Spin Period | CEU Setting |
| --- | --- | --- | --- |
| CSS0 | 4.178789346 | 14.35822556 | 57432 |
| CSS1 | 4.178482987 | 14.35927828 | 57437 |
| CSS2 | 4.178177762 | 14.36032726 | 57441 |
| CSS3 | 4.179342843 | 14.35632401 | 57425 |
| Average | 4.178698235 | 14.35853878 | 57433 |

| CSS Angle TLM | 2.30444 |  |
| --- | --- | --- |
| CSS Sun-Pointing Angle | 4.60888 |  |
|  |  | 30 Mar 16 @1949 |
| CSS Angle TLM | 0.20842 |  |
| CSS Sun-Pointing Angle | 0.41684 |  |
|  |  | 01 Apr 16 @0300 |
| Pre-Burn |  |  |
| Thruster 1 | 9360 | 30 Mar 16 @1949 |
| Thruster 2 | 9104 |  |
| Thruster 3 | 11600 |  |
| Thruster 4 | 11856 |  |
| Post-Burn |  |  |
| Thruster 1 | 9568 | 01 Apr 16 @0300 |
| Thruster 2 | 9280 |  |
| Thruster 3 | 11904 |  |
| Thruster 4 | 12192 |  |
| Number of Pulses |  |  |
| Thruster 1 | 208 |  |
| Thruster 2 | 176 |  |
| Thruster 3 | 304 |  |
| Thruster 4 | 336 |  |
| Thruster Pairs |  |  |
| Thruster 1 & 2 | 384 |  |
| Thruster 3 & 4 | 640 |  |