IBEX Goat Herder  5 Apr 16

The Apogee contacts for Orbit# 322 were nominal for command telemetry and the sun maneuver successful.

The following objectives were completed

- CAR# 819  Download additional star tracker images

  - We were unable to maintain lock at 40ksps, so the star tracker image was dumped at 2ksps over (2) 90min contacts

  - Set star tracker JPEG quality to 95%:

AKT_SetStcmdParmld 74, 1, 0x5f

  - Dump system parameters to confirm setting:

AKT_SetStcmdStatReq

  - Per procedure S924-OP31212, run the star tracker image dump script:

FTG_ModifyTGRate (200,60,1,360,23)

FTG_ModifyTGRate (201,60,5,360,27)

ops_acs_tracker_image.scr  (Select “JPEG” when prompted)

AKT_SetStcmdMemdump (393,xxxxxx) to request missing data packets

- CAR# 820  CSS_Telemetry/Set CEU default spin period

  - We were unable to maintain lock at 40ksps, so the CSS Telemetry was gathered at 2ksps for 25 minutes

css_telemetry_v002.scr

%constraint off

%conversion off

@CEU_SET_PARAMETER (57369, 124)

%conversion on

%constraint on

| CSS Angle TLM | 3.43256 | 5 Apr 16 @1932 |
| --- | --- | --- |
| CSS Sun-Pointing Angle | 6.86512 |  |
| CSS Angle TLM | 1.08822 | 5 Apr 16 @2200 |
| CSS Sun-Pointing Angle | 2.17644 |  |
| Pre-Burn |  |  |
| Thruster 1 | 9568 | 5 Apr 16 @1932 |
| Thruster 2 | 9280 |  |
| Thruster 3 | 11904 |  |
| Thruster 4 | 12192 |  |
| Post-Burn |  |  |
| Thruster 1 | 9840 | 5 Apr 16 @2200 |
| Thruster 2 | 9552 |  |
| Thruster 3 | 12256 |  |
| Thruster 4 | 12544 |  |
| Number of Pulses |  |  |
| Thruster 1 | 272 |  |
| Thruster 2 | 272 |  |
| Thruster 3 | 352 |  |
| Thruster 4 | 352 |  |
| Thruster Pairs |  |  |
| Thruster 1 & 2 | 544 |  |
| Thruster 3 & 4 | 704 |  |