IBEX Goat Herder  24 Apr 16

The Apogee Contacts for Orbit# 324 were nominal for command/telemetry and the sun maneuver successful.

The BCR had a processor reset ( not power cycled)  and the following was observed

- BCR Uptime= 367844

- Gyro Inhibit= YELLOW Inhibited

- CEU5V=OFF

- PCM-B=OFF

HMLOGS= the ACS count increased from 2 to 4

The following objectives were completed

- CAR# 832       BCR Software Recovery 24 Apr 16

  - Run procedure S924-OP31502, IBEX Change Heater Setpoints Procedure to change the setpoints listed. The script will need to be performed up to 6 times to change tank1, tank1, zone1, zone2, zone3, and zone4 to each trip off to 18 and trip on to 16.

  - @ECT_DisableSolarArrayRPT

  - @ECT_TMSAPowerCntl – verify in telemetry that ECT_PowControl is either CURRENT or VOLTAGE

  - @ECT_SetRelay CEU_SAFE, ON   (to make the telemetry reflect reality)

  - @ECT_SetRelay PCM_28V2, ON    (to make the telemetry reflect reality)

  - S924-OP31205 (Turn On/Off Gyro Procedure).

- CAR# 831   CSS_Telemetry/Set CEU default spin period quaternerion_telemetry.scr

CEU_SET_PARAMETER (57445,124) @1559 UTC

The new CSS-based CEU default spin rate is :57445

|  | Spin Rate | Spin Period | CEU Setting |
| --- | --- | --- | --- |
| CSS0 | 4.178713818 | 14.35848508 | 57433 |
| CSS1 | 4.177282523 | 14.36340484 | 57453 |
| CSS2 | 4.177266194 | 14.36346099 | 57453 |
| CSS3 | 4.178175427 | 14.36033528 | 57441 |
| Average | 4.177859491 | 14.36142155 | 57445 |
| CSS Angle TLM | 1.5925 |  |
| CSS Sun-Pointing Angle | 3.185 |  |
|  |  | 19 Apr 16 @0930 |
| CSS Angle TLM | 1.07611 |  |
| CSS Sun-Pointing Angle | 2.15222 |  |
|  |  | 24 Apr 16@1300 |
| Pre-Burn |  |  |
| Thruster 1 | 10512 | 19 Apr 16 @0930 |
| Thruster 2 | 10176 |  |
| Thruster 3 | 13296 |  |
| Thruster 4 | 13632 |  |
| Post-Burn |  |  |
| Thruster 1 | 10752 | 24 Apr 16@1300 |
| Thruster 2 | 10416 |  |
| Thruster 3 | 13664 |  |
| Thruster 4 | 14000 |  |
| Number of Pulses |  |  |
| Thruster 1 | 240 |  |
| Thruster 2 | 240 |  |
| Thruster 3 | 368 |  |
| Thruster 4 | 368 |  |
| Thruster Pairs |  |  |
| Thruster 1 & 2 | 480 |  |
| Thruster 3 & 4 | 736 |  |