IBEX Goat Herder  29 Apr 16

The Perigee Contacts for Orbit# 324 were nominal for command/telemetry and the sun maneuver successful.

The following objectives were completed

- Reset_master_timer.scr

- CAR# 835 Star Tracker Image Dump

@AKT_SetStcmdParmld 120,1,0X19

@AKT_SetStcmdStatReq

ops_acs_tracker_image.scr (jpeg)

74% valid, CCD temp 6.8329  @0321 UTC

64% valid, CCD temp 7.52892 @0432 UTC

0% valid, CCD temp 8.97791 @0559 UTC

0% valid, CCD temp 9.73186 @0759 UTC

- CAR# 834   CSS Telemetry/Set CEU default spin period

quaternerion_telemetry.scr

CEU_SET_PARAMETER (57363,124) @0343 UTC

The new CSS-based CEU default spin rate is :57363

|  | Spin Rate | Spin Period | CEU Setting |
| --- | --- | --- | --- |
| CSS0 | 4.182004707 | 14.34718615 | 57388 |
| CSS1 | 4.184573044 | 14.33838037 | 57353 |
| CSS2 | 4.182101324 | 14.34685469 | 57387 |
| CSS3 | 4.186706782 | 14.33107288 | 57324 |
| Average | 4.183846464 | 14.34087352 | 57363 |

| CSS Angle TLM | 2.77925 |  |
| --- | --- | --- |
| CSS Sun-Pointing Angle | 5.5585 |  |
|  |  | 27 Apr 16@2000 |
| CSS Angle TLM | 1.07611 |  |
| CSS Sun-Pointing Angle | 2.15222 |  |
|  |  | 29 Apr 16 @0300 |
| Pre-Burn |  |  |
| Thruster 1 | 10752 | 27 Apr 16@2000 |
| Thruster 2 | 10416 |  |
| Thruster 3 | 13664 |  |
| Thruster 4 | 14000 |  |
| Post-Burn |  |  |
| Thruster 1 | 10928 | 29 Apr 16 @0300 |
| Thruster 2 | 10592 |  |
| Thruster 3 | 14032 |  |
| Thruster 4 | 14368 |  |
| Number of Pulses |  |  |
| Thruster 1 | 176 |  |
| Thruster 2 | 176 |  |
| Thruster 3 | 368 |  |
| Thruster 4 | 368 |  |
| Thruster Pairs |  |  |
| Thruster 1 & 2 | 352 |  |
| Thruster 3 & 4 | 736 |  |