IBEX Goat Herder  8 May 16

The Perigee Contacts for Orbit# 325 were nominal for command/telemetry and the sun maneuver successful.

The following objectives were completed

- Reset_master_timer.scr

- CAR# 839 Upload Orbit# 327 ATS

IBEX_2016_138_o0327a_Recovery_v001.scr (876-965)

- CAR# 841   CSS Telemetry/Set CEU default spin period

quaternerion_telemetry.scr

CEU_SET_PARAMETER (57478,124) @0343 UTC

The new CSS-based CEU default spin rate is :57478 (looks like there were spin-down pulses)

|  | Spin Rate | Spin Period | CEU Setting |
| --- | --- | --- | --- |
| CSS0 | 4.178647998 | 14.35871124 | 57434 |
| CSS1 | 4.170036062 | 14.38836478 | 57553 |
| CSS2 | 4.176001071 | 14.36781241 | 57471 |
| CSS3 | 4.177248445 | 14.36352201 | 57454 |
| Average | 4.175483394 | 14.36960261 | 57478 |

| CSS Angle TLM | 2.14119 | 5 May 16@1700 |
| --- | --- | --- |
| CSS Sun-Pointing Angle | 4.28238 |  |
| CSS Angle TLM | 0.411169 | 7 May 16 @1900 |
| CSS Sun-Pointing Angle | 0.822338 |  |
| Pre-Burn |  |  |
| Thruster 1 | 11152 | 5 May 16 @1700 |
| Thruster 2 | 10816 |  |
| Thruster 3 | 14384 |  |
| Thruster 4 | 14720 |  |
| Post-Burn |  |  |
| Thruster 1 | 11376 | 7 May 16 @1900 |
| Thruster 2 | 11008 |  |
| Thruster 3 | 14704 |  |
| Thruster 4 | 15072 |  |
| Number of Pulses |  |
| Thruster 1 | 224 |  |
| Thruster 2 | 192 |  |
| Thruster 3 | 320 |  |
| Thruster 4 | 352 |  |
| Thruster Pairs |  |
| Thruster 1 & 2 | 416 |  |
| Thruster 3 & 4 | 672 |  |