IBEX Goat Herder  13 May 16

The Apogee Contacts for Orbit# 326 were nominal for command/telemetry and the sun maneuver successful.

The CEU default spin period was set and the SSR WRT/RD pointers reset

The following objectives were completed

- CAR# 840 Upload Orbit# 327 IBEX_Hi Gain Test

IBEX_2016_138_o0327a_HGC_v001.scr (970-34)

- CAR# 842  Upload Orbit# 326 APL-18 SSR Dump Commands

IBEX_2016_129_o0326a_SSR_v002.scr (968,969)

- CAR# 844 Orbit# 326 APOGEE SSR Read and Write Pointers

@1245 WR:59508   RD:40629

@1251  WR:59521

@CEU_SSR_SET_WRT_PTR(6500)

@CEU_SSR_SET_RD_PTR(6500)

@1402 WR:6826   RD:6500

- CAR# 843   CSS Telemetry/Set CEU default spin period

quaternerion_telemetry.scr

CEU_SET_PARAMETER (57376,124) @1349 UTC

The new CSS-based CEU default spin rate is :57376

|  | Spin Rate | Spin Period | CEU Setting |
| --- | --- | --- | --- |
| CSS0 | 4.184212275 | 14.33961665 | 57358 |
| CSS1 | 4.184065246 | 14.34012055 | 57360 |
| CSS2 | 4.18105765 | 14.35043595 | 57401 |
| CSS3 | 4.1821234 | 14.34677896 | 57387 |
| Average | 4.182864643 | 14.34423803 | 57376 |

| CSS Angle TLM | 0.172459 | 8 Apr 16 @ 1100 |
| --- | --- | --- |
| CSS Sun-Pointing Angle | 0.344918 |  |
| CSS Angle TLM | 0.260196 | 13 Apr 16 @1300 |
| CSS Sun-Pointing Angle | 0.520392 |  |
| Pre-Burn |  |  |
| Thruster 1 | 11376 | 5 Apr 16 @1932 |
| Thruster 2 | 11008 |  |
| Thruster 3 | 14704 |  |
| Thruster 4 | 15072 |  |
| Post-Burn |  |  |
| Thruster 1 | 11616 | 13 Apr 16 @1300 |
| Thruster 2 | 11248 |  |
| Thruster 3 | 15120 |  |
| Thruster 4 | 15488 |  |
| Number of Pulses |  |  |
| Thruster 1 | 240 |  |
| Thruster 2 | 240 |  |
| Thruster 3 | 416 |  |
| Thruster 4 | 416 |  |
| Thruster Pairs |  |  |
| Thruster 1 & 2 | 480 |  |
| Thruster 3 & 4 | 832 |  |