IBEX Goat Herder  17 May 16

The Perigee Contact for Orbit# 326 were nominal for command/telemetry and the sun maneuver successful.

The CEU default spin period was set and the FC dumped

The SSR will be dumped through APL-18

The following objectives were completed

- reset_master_timer.scr

- ops_set_sc_time.scr

- @FMI_SetDownlink (40k)

- @FTG_DumpBackorbit (from start,0,0,0,0)

- CAR# 845   CSS Telemetry/Set CEU default spin period

quaternerion_telemetry.scr

CEU_SET_PARAMETER (572986,124) @0504 UTC

The new CSS-based CEU default spin rate is :57298

|  | Spin Rate | Spin Period | CEU Setting |
| --- | --- | --- | --- |
| CSS0 | 4.187286063 | 14.32909027 | 57316 |
| CSS1 | 4.189222502 | 14.32246675 | 57289 |
| CSS2 | 4.186813002 | 14.33070929 | 57322 |
| CSS3 | 4.190871909 | 14.31682984 | 57267 |
| Average | 4.188548369 | 14.32477404 | 57298 |
| CSS Angle TLM | 0.678685 | 13 May 16 @1300 |
| CSS Sun-Pointing Angle | 1.35737 |  |
| CSS Angle TLM | 0.508989 | 17 May 16 @0430 |
| CSS Sun-Pointing Angle | 1.017978 |  |
| Pre-Burn |  |  |
| Thruster 1 | 11616 | 13 May 16 @1300 |
| Thruster 2 | 11248 |  |
| Thruster 3 | 15120 |  |
| Thruster 4 | 15488 |  |
| Post-Burn |  |  |
| Thruster 1 | 11792 | 17 May 16 @0430 |
| Thruster 2 | 11424 |  |
| Thruster 3 | 15440 |  |
| Thruster 4 | 15808 |  |
| Number of Pulses |  |  |
| Thruster 1 | 176 |  |
| Thruster 2 | 176 |  |
| Thruster 3 | 320 |  |
| Thruster 4 | 320 |  |
| Thruster Pairs |  |  |
| Thruster 1 & 2 | 352 |  |
| Thruster 3 & 4 | 640 |  |