IBEX Goat Herder  5 June 16

The Perigee Contacts for Orbit# 328 were nominal for command/telemetry and the inertial maneuver successful.

The following objectives were completed

- Reset_master_timer.scr

- CAR# 855 Upload Orbit# 330 ATS

IBEX_2016_166_o0330a_v001.scr (550-647)

- CAR# 854 Reset SSR RD/WRT Pointers

SSR_Dump.scr (new) VC2=33374 with 2 errors

CEU_SSR_SET_WRT_PTR (6500)

CEU_SSR_SET_RD_PTP (6500)

- Ops_set_sc_time.scr

- CAR# 856   CSS Telemetry/Set CEU default spin period

quaternerion_telemetry.scr

CEU_SET_PARAMETER (57295,124) @0527 UTC

The new CSS-based CEU default spin rate is :57295

|  | Spin Rate | Spin Period | CEU Setting |
| --- | --- | --- | --- |
| CSS0 | 4.1885365 | 14.3248125 | 57299 |
| CSS1 | 4.19126462 | 14.31548839 | 57261 |
| CSS2 | 4.18729106 | 14.32907317 | 57316 |
| CSS3 | 4.187942752 | 14.32684341 | 57307 |
| Average | 4.188758733 | 14.32405437 | 57295 |
| CSS Angle TLM | 1.376 | 31 May 16 @1200 |
| CSS Sun-Pointing Angle | 2.752 |  |
| CSS Angle TLM | 0.453703 | 4 June 16 @1800 |
| CSS Sun-Pointing Angle | 0.907406 |  |
| Pre-Burn |  |  |
| Thruster 1 | 12400 | 31 May 16 @1200 |
| Thruster 2 | 12000 |  |
| Thruster 3 | 16368 |  |
| Thruster 4 | 16768 |  |
| Post-Burn |  |  |
| Thruster 1 | 12640 | 4 June 16 @1800 |
| Thruster 2 | 12240 |  |
| Thruster 3 | 16672 |  |
| Thruster 4 | 17072 |  |
| Number of Pulses |  |  |
| Thruster 1 | 240 |  |
| Thruster 2 | 240 |  |
| Thruster 3 | 304 |  |
| Thruster 4 | 304 |  |
| Thruster Pairs |  |  |
| Thruster 1 & 2 | 480 |  |
| Thruster 3 & 4 | 608 |  |