IBEX Goat Herder  30 July 16

The Perigee Contacts for Orbit# 334 were nominal for command/telemetry and the inertial maneuver successful.

The following objectives were completed

- Set_Downlink(40k)

- Reset_master_timer.scr

- Ops_set_sc_time.scr

- CAR# 864 Upload ATS

IBEX_2016_221_o0336a_v001.scr (840-955)

- Reset_TaskRawFailed (AC_FDC)

- SSR_Dump.scr (new)

- Set_Relay (stx,off)

| J2000 | Spin Axis |
| --- | --- |
| ECI X | -0.566137 |
| ECI Y | 0.756537 |
| ECI Z | 0.327322 |
| Precession Maneuver |
| MPS Diff | 0.603 | deg |
|  | MPS Diff should be < 1.5 |  |

| -0.23253900 | ActNor.EstInrToBdy[0] |
| --- | --- |
| -0.53128600 | ActNor.EstInrToBdy[1] |
| -0.40181000 | ActNor.EstInrToBdy[2] |
| 0.70866800 | ActNor.EstInrToBdy[3] |
| 1153839854.000 | ActNor.EstTime |

| Right Ascension - RA | 126.809 | deg |
| --- | --- | --- |
| Declination - DEC | 19.106 | deg |
| IBEX Spin Axis vs. Sun Vector |
| IBEX Sun Angle | -2.421 | deg |

MPS  Generated Target VEctors

| MPS Cmd Vector X | -0.570424000 |
| --- | --- |
| MPS Cmd Vector Y | 0.757390000 |
| MPS Cmd Vector Z | 0.317768000 |

| CSS Angle TLM | 0.601008 | 25 July 16 @1300 |
| --- | --- | --- |
| CSS Sun-Pointing Angle | 1.202016 |  |
| CSS Angle TLM | 0.318367 | 29 July 16 @1500 |
| CSS Sun-Pointing Angle | 0.636734 |  |
| Pre-Burn | 25 July 16 @1300 |  |
| Thruster 1 | 15664 |  |
| Thruster 2 | 15168 |  |
| Thruster 3 | 19856 |  |
| Thruster 4 | 20352 |  |
| Post-Burn | 29 July 16 @1500 |  |
| Thruster 1 | 15936 |  |
| Thruster 2 | 15440 |  |
| Thruster 3 | 20160 |  |
| Thruster 4 | 20656 |  |
| Number of Pulses |  |  |
| Thruster 1 | 272 |  |
| Thruster 2 | 272 |  |
| Thruster 3 | 304 |  |
| Thruster 4 | 304 |  |
| Thruster Pairs |  |  |
| Thruster 1 & 2 | 544 |  |
| Thruster 3 & 4 | 608 |  |