IBEX Goat Herder  16 July 16

The Apogee contact for Orbit# 333 was nominal for command/telemetry and the inertial maneuver successful

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Saturday, July 16, 2016	198	1000	USHI01	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	46 asc	2ksps	213 watts

EBNO Values	EBNO Values 3	AGC Strength

@1000=12.81-14.80db (2k)	@1000=-114.64 db

EBNO Values 2	AGC Strength 2

@1002=0.0 (40k)

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

199	2	0	0	0	0

VC 2 Write Pointer 	43037	VC 2 Write Pointer End	43094

VC 2 Read Pointer 	31596	VC 2 Read Pointer End	31596

Orbit# 333 Apogee Contact

@FMI_SetDownlink (40k)

@FMI_SetDownlink (2k)

@Ect_Set Relay (stx, off)

IBEX Orbit# 333 Apogee Contact  16 July 16

J2000	Spin Axis

ECI X	-0.366960

ECI Y	0.853675

ECI Z	0.369567

Precession Maneuver

MPS Diff	0.651	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	113.261	deg

Declination - DEC	21.689	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-2.783	deg

-0.30241900	ActNor.EstInrToBdy[0]

-0.47303200	ActNor.EstInrToBdy[1]

-0.46450600	ActNor.EstInrToBdy[2]

0.68484900	ActNor.EstInrToBdy[3]

1152700000.000	ActNor.EstTime

Orbit# 333 MPS Generated Target Vectors

MPS Cmd Vector X	-0.372176000

MPS Cmd Vector Y	0.855620000

MPS Cmd Vector Z	0.359720000

| CSS Angle TLM | 1.99596 | 11 July 16 @2045 |
| --- | --- | --- |
| CSS Sun-Pointing Angle | 3.99192 |  |
| CSS Angle TLM | 0.590498 | 16 July 16 @1000 |
| CSS Sun-Pointing Angle | 1.180996 |  |
| Pre-Burn |  |  |
| Thruster 1 | 14832 | 11 July 16 @2045 |
| Thruster 2 | 14368 |  |
| Thruster 3 | 19024 |  |
| Thruster 4 | 19488 |  |
| Post-Burn |  |  |
| Thruster 1 | 15088 | 16 July 16 @1000 |
| Thruster 2 | 14624 |  |
| Thruster 3 | 19312 |  |
| Thruster 4 | 19776 |  |
| Number of Pulses |  |  |
| Thruster 1 | 256 |  |
| Thruster 2 | 256 |  |
| Thruster 3 | 288 |  |
| Thruster 4 | 288 |  |
| Thruster Pairs |  |  |
| Thruster 1 & 2 | 512 |  |
| Thruster 3 & 4 | 576 |  |