IBEX Goat Herder  3 Aug 16

The Apogee contact for Orbit# 335 was nominal for command/telemetry and the inertial maneuver successful.

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Wednesday, August 03, 2016	216	1300	USHI01	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	Apogee	2ksps	217 watts

EBNO Values	EBNO Values 3	AGC Strength

@1300=9.04-1182db(2k)	@1300=-115db(2k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

220	1	0	0	0	0

VC 2 Write Pointer 	27536	VC 2 Write Pointer End	27600

VC 2 Read Pointer 	14666	VC 2 Read Pointer End	14666

Orbit# 335 Apogee Tracking Contact

IBEX Orbit# 335 Apogee Target Vectors 3 Aug 16

J2000	Spin Axis

ECI X	-0.628985

ECI Y	0.714075

ECI Z	0.307368

Precession Maneuver

MPS Diff	0.478	deg

*MPS Diff should be < 1.5*

-0.47785000	ActNor.EstInrToBdy[0]

-0.34347500	ActNor.EstInrToBdy[1]

0.07983130	ActNor.EstInrToBdy[2]

0.80455600	ActNor.EstInrToBdy[3]

1154260000.000	ActNor.EstTime

Right Ascension - RA	131.375	deg

Declination - DEC	17.901	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-2.580	deg

IBEX MPS Generated  Target Vectors

MPS Cmd Vector X	-0.629889000

MPS Cmd Vector Y	0.716635000

MPS Cmd Vector Z	0.299457000

CSS Angle TLM	0.318367	29 July 16 @1500

CSS Sun-Pointing Angle	0

CSS Angle TLM	0.655513	03 Aug 16 @1300

CSS Sun-Pointing Angle	1.311026

Pre-Burn	29 July 16 @1500

Thruster 1	15936

Thruster 2	15440

Thruster 3	20160

Thruster 4	20656

Post-Burn	03 Aug 16 @1300

Thruster 1	16192

Thruster 2	15696

Thruster 3	20464

Thruster 4	20960

Number of Pulses

Thruster 1	256

Thruster 2	256

Thruster 3	304

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	512

Thruster 3 & 4	608