IBEX Goat Herder  08 Aug 16

The Orbit# 335 Perigee contacts were nominal for command/telemetry and the inertial maneuver successful

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Sunday, August 07, 2016	220	1700	USHI01	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	13 desc	160ksps	191 watts

EBNO Values	EBNO Values 3	AGC Strength

@1700=7.54-8.44db(160k)	@1700=-107.25db(160k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1896	1	0	0	25644	0

VC 2 Write Pointer 	40291	VC 2 Write Pointer End	6584

VC 2 Read Pointer 	14666	VC 2 Read Pointer End	6500

Orbit# 335 Perigee Contact/reset_master_timer.scr/SSR_Dump.scr (new, PTR Reset)

IBEX Orbit# 335 PERIGEE Target Vectors  7 Aug 16

J2000	Spin Axis

ECI X	-0.682742

ECI Y	0.670715

ECI Z	0.289836

Precession Maneuver

MPS Diff	0.660	deg

*MPS Diff should be < 1.5*

-0.22389400	ActNor.EstInrToBdy[0]

-0.55222600	ActNor.EstInrToBdy[1]

-0.30630200	ActNor.EstInrToBdy[2]

0.74235900	ActNor.EstInrToBdy[3]

1154620000.000	ActNor.EstTime

Right Ascension - RA	135.509	deg

Declination - DEC	16.848	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-2.484	deg

IBEX Orbit# 335 MPS Generated Target Vectors

MPS Cmd Vector X	-0.688092000

MPS Cmd Vector Y	0.669538000

MPS Cmd Vector Z	0.279728000

CSS Angle TLM	1.88263	03 Aug 16 @1336

CSS Sun-Pointing Angle	3.76526

CSS Angle TLM	0.422436	07 Aug 16 @1700

CSS Sun-Pointing Angle	0.844872

CSS Angle TLM	1.88263	03 Aug 16 @1336

CSS Sun-Pointing Angle	3.76526

CSS Angle TLM	0.422436	07 Aug 16 @1700

CSS Sun-Pointing Angle	0.844872

Pre-Burn

Thruster 1	16192	03 Aug 16 @1336

Thruster 2	15696

Thruster 3	20464

Thruster 4	20960

Post-Burn

Thruster 1	16448	07 Aug 16 @1700

Thruster 2	15952

Thruster 3	20752

Thruster 4	21248

Number of Pulses

Thruster 1	256

Thruster 2	256

Thruster 3	288

Thruster 4	288

Thruster Pairs

Thruster 1 & 2	512

Thruster 3 & 4	576

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Monday, August 08, 2016	221	0600	AUWA	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	10 asc	160ksps	240 watts

EBNO Values	EBNO Values 3	AGC Strength

@0600=9.30-10.20db(160k)	@0600=-99.96db(160k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1168	1	1307	0	0	0

VC 2 Write Pointer 	7089	VC 2 Write Pointer End	7118

VC 2 Read Pointer 	6500	VC 2 Read Pointer End	6500

Orbit# 335 Tracking Contact/@FTG_DumpBackorbit (from start,0,0,0,0)/stx,off