IBEX Goat Herder 12 Sept 16

The Perigee contacts for Orbit# 339 were nominal for command/telemetry and the inertial maneuver successful.

The IBEX_Lo star sensor telemetry was increased

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Monday, September 12, 2016	256	1100	USHI01	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

TPerry	11 desc	160ksps

EBNO Values	EBNO Values 3	AGC Strength

9.7 -> 10.3 @160k	-104

EBNO Values 2	AGC Strength 2

7.3 -> 7.7 @320k

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1902	3	0	0	19665	0

VC 2 Write Pointer 	0	VC 2 Write Pointer End	26190

VC 2 Read Pointer 	0	VC 2 Read Pointer End	26165

Commanded to 320 k

SSR dump -> New

Reset Master Timer

Set SC Clock

Reset FDC Totals

Maneuver was nominal

Q1 -0.59039000 ActNor.EstInrToBdy[0]

Q2 -0.32870900 ActNor.EstInrToBdy[1]

Q3 0.56108000 ActNor.EstInrToBdy[2]

Q4 0.47810100 ActNor.EstInrToBdy[3]

GPS sec 1157713839.000 ActNor.EstTime

MPS Diff 0.662

MPS Cmd Vector X -0.977190000

MPS Cmd Vector Y 0.198474000

MPS Cmd Vector Z 0.075553000

CSS Angle TLM 1.04978 8 Sept 16 @1000

CSS Sun-Pointing Angle 2.09956

CSS Angle TLM 0.588174 12 Sept 16 @1100

CSS Sun-Pointing Angle 1.176348

Pre-Burn 8 Sept 16 @1000

Thruster 1 18288

Thruster 2 17728

Thruster 3 22880

Thruster 4 23440

Post-Burn 12 Sept 16 @1100

Thruster 1 18528

Thruster 2 17968

Thruster 3 23152

Thruster 4 23712

Number of Pulses

Thruster 1 240

Thruster 2 240

Thruster 3 272

Thruster 4 272

Thruster Pairs

Thruster 1 & 2 480

Thruster 3 & 4 544

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Monday, September 12, 2016	256	2100	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	868	872	10 asc	320ksps	177 watts

EBNO Values	EBNO Values 3	AGC Strength

@2101=7.27-7.37db(320k)	@2101=-105.34db (320k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1521	1	1295	0	0	0

VC 2 Write Pointer 	26409	VC 2 Write Pointer End	26440

VC 2 Read Pointer 	26165	VC 2 Read Pointer End	26165

Orbit# 339 Perigee Contact/CAR# 872 Upload Orbit# 341 ATS 1. IBEX_2016_265_o0341a_v002.scr (612-710)/ CAR# 868 Change Star

Sensor telemetry rate to nominal rate

%constraint off

%conversion off

@CEU_SET_PARAMETER 16, 123

%conversion on

%constraint on

@CEU_SET_PARAMETER 64, LO_STAR_HISTO_CADENCE

@CEU_SET_PARAMETER 123, ROUND_ROBIN_START

@CEU_SET_PARAMETER 123, ROUND_ROBIN_END

@CEU_SET_PARAMETER 3, ROUND_ROBIN_START

@CEU_SET_PARAMETER 3, ROUND_ROBIN_END

@CEU_SET_PARAMETER 0, ROUND_ROBIN_START

@CEU_SET_PARAMETER 128, ROUND_ROBIN_END