IBEX Goat Herder  14 Oct 16

The Apogee contact for Orbit# 344 was nominal for command/telemetry and the inertial maneuver successful.

The IBEX_Hi Gain Test ATS was uploaded (881-944)

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Friday, October 14, 2016	288	0830	USHI01	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	876	45 desc	2ksps	231 watts

EBNO Values	EBNO Values 3	AGC Strength

@0831=18.94-20.15db(2k)	@0831=-116.53db(2k)

EBNO Values 2	AGC Strength 2

@0832=4.19-6.27db(40k)	@0832=-115.08db(40k)

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

657	8	1442	30	0	0

VC 2 Write Pointer 	17894	VC 2 Write Pointer End	17968

VC 2 Read Pointer 	6500	VC 2 Read Pointer End	6500

Orbit# 343 Apogee Contact

@FMI_SetDownlink(40k)

@FTG_DumpBackorbit (from start,0,0,0,0)

CAR# 876 Upload Orbit# 344 IBEX_Hi  Gain Test 1.IBEX_2016_292_o0344a_HGC_V001.scr (881-944)

IBEX Orbit# 344 APOGEE Target Vectors

J2000	Spin Axis

ECI X	-0.952435

ECI Y	-0.280134

ECI Z	-0.119969

Precession Maneuver

MPS Diff	0.793	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	196.390	deg

Declination - DEC	-6.890	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.705	deg

0.72930500	ActNor.EstInrToBdy[0]

-0.16762600	ActNor.EstInrToBdy[1]

-0.57828200	ActNor.EstInrToBdy[2]

0.32497000	ActNor.EstInrToBdy[3]

1160470000.000	ActNor.EstTime

IBEX MPS Generated Target Vectors

MPS Cmd Vector X	-0.950089000

MPS Cmd Vector Y	-0.281988000

MPS Cmd Vector Z	-0.133467000

CSS Angle TLM	0.771771	09 Oct 16 @1600

CSS Sun-Pointing Angle	1.543542

CSS Angle TLM	0.888367	14 Oct 16 @0830

CSS Sun-Pointing Angle	0

Pre-Burn	09 Oct 16 @1600

Thruster 1	20208

Thruster 2	19568

Thruster 3	24912

Thruster 4	25552

Post-Burn	14 Oct 16@0830

Thruster 1	20464

Thruster 2	19824

Thruster 3	25200

Thruster 4	25840

Number of Pulses

Thruster 1	256

Thruster 2	256

Thruster 3	288

Thruster 4	288

Thruster Pairs

Thruster 1 & 2	512

Thruster 3 & 4	576