IBEX Goat Herder  23 Oct 16

The second Apogee contact for Orbit# 344 was nominal for command/telemetry and the inertial maneuver successful

A RAZOR and PR will be opened to address the earlier INP2 file transfer problem

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Sunday, October 23, 2016	297	0711	USHI01	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	877	44 desc	2ksps	123 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

513	1	0	0	0	0

VC 2 Write Pointer 	37690	VC 2 Write Pointer End	37741

VC 2 Read Pointer 	27025	VC 2 Read Pointer End	27025

1.	Blind_acq.scr (2k)

2.	Set Relay,stx,off (104)

3.	SetDownlink (40k)

4.	 CAR# 877 Upload ATS

IBEX_20130o0345a_v001.scr (105-197)

5.	 Stx,off

IBEX Orbit# 344 APOGEE Target Vectors  23 Oct 16

J2000	Spin Axis

ECI X	-0.893407

ECI Y	-0.412205

ECI Z	-0.178636

Precession Maneuver

MPS Diff	0.726	deg

*MPS Diff should be < 1.5*

0.66284600	ActNor.EstInrToBdy[0]

-0.38723800	ActNor.EstInrToBdy[1]

-0.36700900	ActNor.EstInrToBdy[2]

0.52534400	ActNor.EstInrToBdy[3]

1161240000.000	ActNor.EstTime

Right Ascension - RA	204.768	deg

Declination - DEC	-10.290	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.609	deg

MPS Generated APOGEE Target Vectors

MPS Cmd Vector X	-0.890065000

MPS Cmd Vector Y	-0.414023000

MPS Cmd Vector Z	-0.190706000

CSS Angle TLM	1.17919

CSS Sun-Pointing Angle	2.35838

18 Oct 16 @1447

CSS Angle TLM	0.92736

CSS Sun-Pointing Angle	1.85472

23 Oct 16 @0711

Pre-Burn

Thruster 1	272	18 Oct 16 @1447

Thruster 2	272

Thruster 3	304

Thruster 4	304

Post-Burn

Thruster 1	560	23 Oct 16 @0711

Thruster 2	560

Thruster 3	608

Thruster 4	608

Number of Pulses

Thruster 1	288

Thruster 2	288

Thruster 3	304

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	576

Thruster 3 & 4	608