IBEX Goat Herder  27 Oct 16

The PERIGEE Tracking contact for Orbit# 344 was nominal for command/telemetry and the inertial maneuver successful.

The SSR data was collected via APL-18

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Thursday, October 27, 2016	301	1820	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	878	14 asc	2ksps	351 watts

EBNO Values	EBNO Values 3	AGC Strength

@1822=19.95-21.00db(2k)	@1822=-114db(2k)

EBNO Values 2	AGC Strength 2

@1823=6.28-7.87db(40k)	@1823=-110.97db(40k)

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

734	5	1446	32	0	0

VC 2 Write Pointer 	47242	VC 2 Write Pointer End	47266

VC 2 Read Pointer 	46910	VC 2 Read Pointer End	46910

Orbit# 344 Perigee Tracking Contact

1. Reset_master_timer.scr

2. CAR# 878 Upload Orbit# 346 ATS v002

IBEX_2016_310_o0346a_v002.scr (299-399)

3. @FTG_DumpBAckorbit(from start,0,0,0,0)

4. stx,off

IBEX Orbit# 344 PERIGEE Target Vectors  27 Oct 17

J2000	Spin Axis

ECI X	-0.854136

ECI Y	-0.478076

ECI Z	-0.204684

Precession Maneuver

MPS Diff	0.745	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	209.237	deg

Declination - DEC	-11.811	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.475	deg

0.73966000	ActNor.EstInrToBdy[0]

0.23504200	ActNor.EstInrToBdy[1]

-0.61770400	ActNor.EstInrToBdy[2]

0.12688500	ActNor.EstInrToBdy[3]

1161630000.000	ActNor.EstTime

CSS Angle TLM	0.92736

CSS Sun-Pointing Angle	1.85472

23 Oct 16 @0711

CSS Angle TLM	0.92736

CSS Sun-Pointing Angle	0.922809

27 Oct 16 @1820

Pre-Burn

Thruster 1	560	23 Oct 16 @0711

Thruster 2	560

Thruster 3	608

Thruster 4	608

Post-Burn

Thruster 1	832	27 Oct 16 @1820

Thruster 2	832

Thruster 3	912

Thruster 4	912

Number of Pulses

Thruster 1	272

Thruster 2	272

Thruster 3	304

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	544

Thruster 3 & 4	608

Orbit# 344 MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	-0.851410000

MPS Cmd Vector Y	-0.477320000

MPS Cmd Vector Z	-0.217411000