IBEX Goat Herder  5 Nov 16

The Perigee contacts for Orbit# 345 were nominal for command/telemetry and the inertial maneuver successful

The SSR data was collected through APL-18

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Saturday, November 05, 2016	310	2100	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	879	16 asc	40ksps	281 watts

EBNO Values	EBNO Values 3	AGC Strength

@2104=3.60-6.40db(40k)	@2103=-117.87db(40k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1132	4	1440	35	0	0

VC 2 Write Pointer 	880	VC 2 Write Pointer End	970

VC 2 Read Pointer 	245	VC 2 Read Pointer End	245

Orbit# 345 Perigee tracking Contact

reset_master_timer.scr

CAR# 879 Upload Orbit# 347 ATS 1.IBEX_2016_319_o0347a_v001.scr (499-597)

IBEX Orbit# 345 PERIGEE Target Vectors  5 Nov 16

J2000	Spin Axis

ECI X	-0.760494

ECI Y	-0.596085

ECI Z	-0.257549

Precession Maneuver

MPS Diff	0.603	deg

MPS Diff should be < 1.5

-0.52025600	ActNor.EstInrToBdy[0]

-0.59842100	ActNor.EstInrToBdy[1]

0.59827600	ActNor.EstInrToBdy[2]

0.11528700	ActNor.EstInrToBdy[3]

1162420000.000	ActNor.EstTime

Right Ascension - RA	218.090	deg

Declination - DEC	-14.925	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.468	deg

MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	-0.759329000

MPS Cmd Vector Y	-0.593125000

MPS Cmd Vector Z	-0.267625000

CSS Angle TLM	1.54611

CSS Sun-Pointing Angle	3.09222

01 Nov 16 @0100

CSS Angle TLM	0.945637

CSS Sun-Pointing Angle	1.891274

05 Nov 16 @2100

Pre-Burn

Thruster 1	1120	01 Nov 16 @0100

Thruster 2	1120

Thruster 3	1184

Thruster 4	1184

Post-Burn

Thruster 1	1456	05 Nov 16 @2100

Thruster 2	1408

Thruster 3	1504

Thruster 4	1552

Number of Pulses

Thruster 1	336

Thruster 2	288

Thruster 3	320

Thruster 4	368

Thruster Pairs

Thruster 1 & 2	624

Thruster 3 & 4	688