IBEX Goat Herder  19 Nov 16

The Orbit# 347 Apogee contact failed for command, and the inertial maneuver was successful.

Unable to send commands. 	agc levels ranged from -119 through -121db and commands were dropped during the attempted ATS upload

RAZOR# 619

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Saturday, November 19, 2016	324	2230	USHI01	619	Fail

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	Apogee	2ksps	200 watts

EBNO Values	EBNO Values 3	AGC Strength

@2231=10.74-15.81db(2k)	@2231=-121db(2k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

217	2	0	0	0	0

VC 2 Write Pointer 	17567	VC 2 Write Pointer End	17625

VC 2 Read Pointer 	6500	VC 2 Read Pointer End	6500

Orbit# 347  APOGEE Contact

Unable to send commands

agc levels ranged from -119 through -121db and commands were dropped during the

ATS upload

IBEX Orbit# 347  APOGEE Target Vectors  19 Nov 16

J2000	Spin Axis

ECI X	-0.585801

ECI Y	-0.743382

ECI Z	-0.322832

Precession Maneuver

MPS Diff	0.630	deg

MPS Diff should be < 1.5

0.18828500	ActNor.EstInrToBdy[0]

-0.79117900	ActNor.EstInrToBdy[1]

0.36123300	ActNor.EstInrToBdy[2]

0.45617400	ActNor.EstInrToBdy[3]

1163630000.000	ActNor.EstTime

Right Ascension - RA	231.761	deg

Declination - DEC	-18.834	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.915	deg

Orbit# 347 MPS Generated APOGEE Target Vectors

MPS Cmd Vector X	-0.581736000

MPS Cmd Vector Y	-0.742102000

MPS Cmd Vector Z	-0.332968000

CSS Angle TLM	0.35277

CSS Sun-Pointing Angle	0.70554

14 Nov 16 @1130

CSS Angle TLM	1.40026

CSS Sun-Pointing Angle	2.80052

19 Nov 16 @2230

Pre-Burn

Thruster 1	2064	14 Nov 16 @1130

Thruster 2	2016

Thruster 3	2272

Thruster 4	2320

Post-Burn

Thruster 1	2240	19 Nov 16 @2230

Thruster 2	2192

Thruster 3	2480

Thruster 4	2528

Number of Pulses

Thruster 1	176

Thruster 2	176

Thruster 3	208

Thruster 4	208

Thruster Pairs

Thruster 1 & 2	352

Thruster 3 & 4	416