IBEX Goat Herder  30 Nov 16

The Apogee tracking contact was successful in confirming the inertial maneuver and Lo Gain Curve test commands.

The contact failed to maintain a command link.

USN/PR# 8842 = USN/HAW02 HPA power output is less than 100 watts

RAZOR# 620= USN/HAW02 reduced power output, unable to command the spacecraft

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Wednesday, November 30, 	335	0100	USHI02	620	8842	Fail

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	41 desc	2ksps	< 100 watts

EBNO Values	EBNO Values 3	AGC Strength

@0102=9.0-14.40db(2ksps)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

89	36	0	0	0	0

VC 2 Write Pointer 	38721	VC 2 Write Pointer End	38762

VC 2 Read Pointer 	26037	VC 2 Read Pointer End	26037

Orbit# 348 Apogee Tracking Contact

unable to maintain the command link

HPA power output is less than 100 watts

IBEX_Lo Gain Curve Test commands were successfully executed

IBEX Orbit# 348  APOGEE Target Vectors

J2000	Spin Axis

ECI X	-0.446719

ECI Y	-0.822567

ECI Z	-0.351888

Precession Maneuver

MPS Diff	0.894	deg

*MPS Diff should be < 1.5*

0.72383700	ActNor.EstInrToBdy[0]

0.38987700	ActNor.EstInrToBdy[1]

-0.47640900	ActNor.EstInrToBdy[2]

0.31159300	ActNor.EstInrToBdy[3]

1164500000.000	ActNor.EstTime

Right Ascension - RA	241.495	deg

Declination - DEC	-20.603	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-4.778	deg

Orbit# 348  MPS Generated APOGEE Target Vectors

MPS Cmd Vector X	-0.441817000

MPS Cmd Vector Y	-0.818934000

MPS Cmd Vector Z	-0.366258000

CSS Angle TLM	2.02129	23 Nov 16 @2000

CSS Sun-Pointing Angle	4.04258

CSS Angle TLM	1.16137	30 Nov 16 @0100

CSS Sun-Pointing Angle	2.32274

Pre-Burn

Thruster 1	2528	23 Nov 16 @2000

Thruster 2	2480

Thruster 3	2800

Thruster 4	2848

Post-Burn

Thruster 1	2880	30 Nov 16 @0100

Thruster 2	2768

Thruster 3	3104

Thruster 4	3216

Number of Pulses

Thruster 1	352

Thruster 2	288

Thruster 3	304

Thruster 4	368

Thruster Pairs

Thruster 1 & 2	640

Thruster 3 & 4	672