IBEX Goat Herder  30 Dec 16

The Perigee tracking contact for Orbit# 351 was nominal for command/telemetry and the inertial maneuver successful.

The SSR will be dumped via APL-18 on 31 Dec 16 @0800 UTC

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Friday, December 30, 2016	365	1200	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	890	12 desc	320ksps	204 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1897	0	1284	0	0	0

VC 2 Write Pointer 	60308	VC 2 Write Pointer End	60345

VC 2 Read Pointer 	34361	VC 2 Read Pointer End	34361

Orbit# 351 Perigee Tracking Contact

- reset_mater_timer.scr

- ops_set_sc_time.scr

- CAR# 890 Upload Orbit# 353 ATS  1. IBEX_2017_009_o0353a_v001 (839-908,920,910-919)

- @FTG_DumpBackorbit (from start,0,0,0,0)

- @ACT_Reset_TaskRawFailed (AC_FDC)

IBEX Orbit# 351 PERIGEE Target Vectors  30 Dec 16

J2000	Spin Axis

ECI X	0.175030

ECI Y	-0.902893

ECI Z	-0.392617

Precession Maneuver

MPS Diff	0.637	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	280.971	deg

Declination - DEC	-23.117	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	0.787	deg

0.76560700	ActNor.EstInrToBdy[0]

-0.33189600	ActNor.EstInrToBdy[1]

0.31140700	ActNor.EstInrToBdy[2]

0.45466200	ActNor.EstInrToBdy[3]

1167140000.000	ActNor.EstTime

MPS Generated Target Vectors

MPS Cmd Vector X	0.181354000

MPS Cmd Vector Y	-0.898202000

MPS Cmd Vector Z	-0.400429000

CSS Angle TLM	0.832277	26 Dec 16 @1930

CSS Sun-Pointing Angle	1.664554

CSS Angle TLM	0.209357	30 Dec 16 @ 1200

CSS Sun-Pointing Angle	0.418714

Pre-Burn

Thruster 1	4864	26 Dec 16 @1930

Thruster 2	4752

Thruster 3	5200

Thruster 4	5312

Post-Burn

Thruster 1	5152	30 Dec 16 @ 1200

Thruster 2	5040

Thruster 3	5536

Thruster 4	5648

Number of Pulses

Thruster 1	288

Thruster 2	288

Thruster 3	336

Thruster 4	336

Thruster Pairs

Thruster 1 & 2	576

Thruster 3 & 4	672