IBEX Goat Herder  6 Feb 17

The Perigee contacts for Orbit# 355 were nominal for command/telemetry and the inertial maneuver successful.

The SSR Data from Orbit# 354 and Orbit# 355 was successfully re-dumped.

We had late AOS on the first Perigee contact due to software/firewall configuration changes at USN.

USN/PR# 9198

RAZOR# 622

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Sunday, February 05, 2017	036	1600	AUWA	9198	Fail

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	895	12 desc	160ksps

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1876	2	0	0	26884	0

VC 2 Write Pointer 	24765	VC 2 Write Pointer End	6519

VC 2 Read Pointer 	24765	VC 2 Read Pointer End	6500

Orbit# 355 Perigee SSR_Dump/Tracking Contact

reset_master_timer.scr

SSR_Dump.scr (new),Reset_SSR_PNTRS(6500)

CAR# 895 Upload Orbit# 357 ATS 1.IBEX_2017_046_o0357a_v003.scr (284-384)

@ECT_SetRelay stx,off (02:06:09:32, 385)

IBEX Orbit# 355 Perigee Target Vector  5 Feb 17

J2000	Spin Axis

ECI X	0.741370

ECI Y	-0.576385

ECI Z	-0.343732

Precession Maneuver

MPS Diff	0.613	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	322.136	deg

Declination - DEC	-20.104	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	5.041	deg

0.69535300	ActNor.EstInrToBdy[0]

-0.43399400	ActNor.EstInrToBdy[1]

0.56980200	ActNor.EstInrToBdy[2]

0.05882190	ActNor.EstInrToBdy[3]

1170350000.000	ActNor.EstTime

Orbit# 355 MPS Generated Target Vectors

MPS Cmd Vector X	0.738917000

MPS Cmd Vector Y	-0.573494000

MPS Cmd Vector Z	-0.353703000

CSS Angle TLM	0.534125	01 Feb 17 @1800

CSS Sun-Pointing Angle	1.06825

CSS Angle TLM	2.05637	05 Feb 17 @1600

CSS Sun-Pointing Angle	4.11274

Pre-Burn

Thruster 1	7856	01 Feb 17 @1800

Thruster 2	7648

Thruster 3	8560

Thruster 4	8768

Post-Burn

Thruster 1	8336	05 Feb 17 @1600

Thruster 2	8128

Thruster 3	9024

Thruster 4	9232

Number of Pulses

Thruster 1	480

Thruster 2	480

Thruster 3	464

Thruster 4	464

Thruster Pairs

Thruster 1 & 2	960

Thruster 3 & 4	928

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Monday, February 06, 2017	037	0800	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	896	13 Asc	160ksps

EBNO Values	EBNO Values 3	AGC Strength

@0759=6.92-5.17db(160k)

EBNO Values 2	AGC Strength 2

@0800=3.72-1.78db(320k)

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1819	2	1298	0	30100	0

VC 2 Write Pointer 	6884	VC 2 Write Pointer End	6912

VC 2 Read Pointer 	6500	VC 2 Read Pointer End	6500

Orbit# 355 Tracking Contact

@FMI_Set_Downlink (320k)

1.CAR# 896 Redump Orbit# 354 and Orbit# 355 Blocks 1.SSR_Dump.scr

(start 33750, NUMBLKS 28900) 1. SSR_Dump.scr (start 89510,NUMBLKS 1200)

@FCH_Del_timedCMD(461)

ops_set_sc_time.scr

@FTG_DumpBAckorbit(from start,0,0,0,0)