IBEX Goat Herder  15 Feb 17

The SSR_Dump/Tracking contact for Orbit# 356 was nominal for command/telemetry and the inertial maneuver successful.

We had late AOS and missed the first 20 minutes of the contact.

The OrbitalATK SFTP server has been intermittently off line, which causes the INP2 file to be manually loaded at the ground station

USN/PR# 9239:Late AOS. Unable to get INP2 tracking files from SFTP server

RAZOR# 625:OrbitalATK SFTP server down

RAZOR# 623:USN unable to push VC data to MAESTRO servers post pass

We were able to dump the entire SSR during the contact, and re-dump 20 blocks from Orbit# 354 (CAR#898)

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Wednesday, February 15, 2017	046	0200	USHI02	625/6	9239	Fail

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	898	12 desc	320ksps	200 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1266	0	0	0	27705	0

VC 2 Write Pointer 	34184	VC 2 Write Pointer End	34203

VC 2 Read Pointer 	6500	VC 2 Read Pointer End	34185

Orbit# 356 SSR_Dump/Tracking Contact

Late AOS/Manual station load of INP2 tracking file

1.reset_master_timer.scr

2.CAR# 898 Re_DumpOrbit# 354 Blks (start-56290,NumBlks-20)

IBEX PERIGEE Target Vectors 15 Feb 17 @0200 UTC

J2000	Spin Axis

ECI X	0.840012

ECI Y	-0.458233

ECI Z	-0.290520

Precession Maneuver

MPS Diff	0.698	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	331.387	deg

Declination - DEC	-16.889	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	4.917	deg

0.75344000	ActNor.EstInrToBdy[0]

-0.27854700	ActNor.EstInrToBdy[1]

0.58932700	ActNor.EstInrToBdy[2]

0.08621950	ActNor.EstInrToBdy[3]

1171160000.000	ActNor.EstTime

MPS Generated Perigee Target Vectors

MPS Cmd Vector X	0.838433000

MPS Cmd Vector Y	-0.453812000

MPS Cmd Vector Z	-0.301804000

CSS Angle TLM	2.66543	10 Feb 17 @1740

CSS Sun-Pointing Angle	5.33086

CSS Angle TLM	1.81348	15 Feb 17 @0200

CSS Sun-Pointing Angle	3.62696

Pre-Burn

Thruster 1	8576	10 Feb 17 @1740

Thruster 2	8368

Thruster 3	9296

Thruster 4	9504

Post-Burn

Thruster 1	9280	15 Feb 17 @0200

Thruster 2	9024

Thruster 3	9968

Thruster 4	10224

Number of Pulses

Thruster 1	704

Thruster 2	656

Thruster 3	672

Thruster 4	720

Thruster Pairs

Thruster 1 & 2	1360

Thruster 3 & 4	1392

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Wednesday, February 15, 2017	046	1400	AUWA	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

TPerry	897	12 asc	40ksps	190

EBNO Values	EBNO Values 3	AGC Strength

3.2 - 6.0 @40 K	-102

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1886	13	0	0	0	0

ATS upload -> IBEX_2017_055_o0358a_v001

102 cmds Trk # 490 - 591