IBEX Goat Herder  20 Feb 17

The Apogee contact for Orbit 357 was nominal for command /telemetry and the inertial maneuver successful

The proficiency contact was taken successfully on  MAESTRO01/CMD1 Workstation

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Monday, February 20, 2017	051	1800	USHI02

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	45 desc	2ksps	195 watts

EBNO Values	EBNO Values 3	AGC Strength

@1800=14.59-15.75db (2k)	@1800=117.69db(2k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

215	2	0	0	0	0

VC 2 Write Pointer 	VC 2 Write Pointer End	51209

VC 2 Read Pointer 	VC 2 Read Pointer End	34185

Orbit# 357 Apogee Tracking Contact

Profeciency contact on IBEX-1 MAESTRO server and CMD1 Workstation

@FMI_SetDownlink(40k)

@FMI_SetDownlink (2k)

IBEX Orbit# 357 APOGEE Target Vectors 20 Feb 17 @1800 UTC

J2000	Spin Axis

ECI X	0.840472

ECI Y	-0.488689

ECI Z	-0.234073

Precession Maneuver

MPS Diff	0.832	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	329.824	deg

Declination - DEC	-13.537	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-5.212	deg

-0.41997800	ActNor.EstInrToBdy[0]

0.66381800	ActNor.EstInrToBdy[1]

-0.54889800	ActNor.EstInrToBdy[2]

0.28578700	ActNor.EstInrToBdy[3]

1171650000.000	ActNor.EstTime

MPS Generated Target Vectors

MPS Cmd Vector X	0.845686000

MPS Cmd Vector Y	-0.485839000

MPS Cmd Vector Z	-0.220851000

CSS Angle TLM	1.81348	15 Feb 17 @0200

CSS Sun-Pointing Angle	3.62696

CSS Angle TLM	1.85477	20 Feb 17 @1800

CSS Sun-Pointing Angle	3.70954

Pre-Burn

Thruster 1	9280	15 Feb 17 @0200

Thruster 2	9024

Thruster 3	9968

Thruster 4	10224

Post-Burn

Thruster 1	9520	20 Feb 17 @1800

Thruster 2	9264

Thruster 3	10208

Thruster 4	10464

Number of Pulses

Thruster 1	240

Thruster 2	240

Thruster 3	240

Thruster 4	240

Thruster Pairs

Thruster 1 & 2	480

Thruster 3 & 4	480