IBEX Goat Herder  15 Mar 17

The Perigee contacts for Orbit# 359 were nominal for command/telemetry and the inertial maneuver successful

The Lo Normal sweep table was successfully loaded tonight at the start of orbit 360 arc a. All systems are nominal

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Tuesday, March 14, 2017	073	1200	AUWA	625	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	901	11 desc	320ksps	233 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1866	1	0	0	26071	0

VC 2 Write Pointer 	32569	VC 2 Write Pointer End	32604

VC 2 Read Pointer 	6500	VC 2 Read Pointer End	32571

Orbit# 359 SSR_Dump/Tracking Contact

reset_master_timer.scr

@FMI_SetDownlink(320ksps)

SSR_Dump.scr (new)

CAR# 901  Upload 	Orbit# 361 ATS 1. IBEX_2017_082_o0361a_v001.scr (155-252)

ops_set_sc_time_scr/

IBEX Orbit# 359 PERIGEE Target Vectors 14 Mar 17

J2000	Spin Axis

ECI X	0.995901

ECI Y	-0.082383

ECI Z	-0.037342

Precession Maneuver

MPS Diff	0.607	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	355.271	deg

Declination - DEC	-2.140	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	0.708	deg

-0.58838100	ActNor.EstInrToBdy[0]

0.41530600	ActNor.EstInrToBdy[1]

-0.59785800	ActNor.EstInrToBdy[2]

0.35198700	ActNor.EstInrToBdy[3]

1173530000.000	ActNor.EstTime

MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	0.996385000

MPS Cmd Vector Y	-0.073345000

MPS Cmd Vector Z	-0.042870000

CSS Angle TLM	0.432658	11 Mar 17 @2000 UTC

CSS Sun-Pointing Angle	0.865316

CSS Angle TLM	0.395648	14 Mar 17 @1200 UTC

CSS Sun-Pointing Angle	0.791296

Pre-Burn

Thruster 1	10976	11 Mar 17 @2000 UTC

Thruster 2	10720

Thruster 3	11728

Thruster 4	11984

Post-Burn

Thruster 1	11264	14 Mar 17 @1200 UTC

Thruster 2	11008

Thruster 3	12016

Thruster 4	12272

Number of Pulses

Thruster 1	288

Thruster 2	288

Thruster 3	288

Thruster 4	288

Thruster Pairs

Thruster 1 & 2	576

Thruster 3 & 4	576

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Wednesday, March 15, 2017	074	0500	USAK	625	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	885	16 asc	64ksps	356 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

846	1	0	0	0	0

VC 2 Write Pointer 	33255	VC 2 Write Pointer End	33348

VC 2 Read Pointer 	32571	VC 2 Read Pointer End	32571

Orbit# 359 Tracking Contact

CAR# 885 IBEX_Lo ISN Sweep Table Upload

- @CEU_MODE (HVENG)

- @CEU_MODE (HVSTANDBY)

- sweep_table_upload_160922 (Table_Lo_12345678_Normal,quit)

- @CEU_MODE (HVENG)

- @CEU_MODE (HVSCI)

- stx,off