IBEX Goat Herder  30 Mar 17

The Apogee Tracking Contact for Orbit# 361 was nominal for command/telemetry and the inertial maneuver successful.

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Thursday, March 30, 2017	089	1730	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	33 Desc	2ksps	180 watts

EBNO Values	EBNO Values 3	AGC Strength

@1730=9.50-13.40db(2ksps)	@1730=-121.04db(2ksps)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

220	1	0	0	0	0

VC 2 Write Pointer 	11041	VC 2 Write Pointer End	11100

VC 2 Read Pointer 	61539	VC 2 Read Pointer End	61539

IBEX Orbit# 361 Apogee Tracking Contact

IBEX Orbit# 361 APOGEE Target Vectors 30 Mar 17

J2000	Spin Axis

ECI X	0.996687

ECI Y	0.073621

ECI Z	0.034558

Precession Maneuver

MPS Diff	0.826	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	4.225	deg

Declination - DEC	1.980	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-5.537	deg

0.17379400	ActNor.EstInrToBdy[0]

0.67269400	ActNor.EstInrToBdy[1]

0.23071600	ActNor.EstInrToBdy[2]

0.68121200	ActNor.EstInrToBdy[3]

1174930000.000	ActNor.EstTime

MPS Generated APOGEE Target Vectors

MPS Cmd Vector X	0.996068000

MPS Cmd Vector Y	0.084833000

MPS Cmd Vector Z	0.025531000

CSS Angle TLM	1.61083	24 Mar 17 @0840 UTC

CSS Sun-Pointing Angle	3.22166

CSS Angle TLM	1.98041	30 Mar 17 @1730 UTC

CSS Sun-Pointing Angle	3.96082

Pre-Burn

Thruster 1	11600	24 Mar 17 @0840 UTC

Thruster 2	11344

Thruster 3	12368

Thruster 4	12624

Post-Burn

Thruster 1	11872	30 Mar 17 @1730 UTC

Thruster 2	11616

Thruster 3	12672

Thruster 4	12928

Number of Pulses

Thruster 1	272

Thruster 2	272

Thruster 3	304

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	544

Thruster 3 & 4	608