IBEX Goat Herder  15 Apr 17

The Apogee tracking contact for Orbit# 363 was nominal for command/telemetry and the sun maneuver successful

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Saturday, April 15, 2017	105	1300	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	45 Desc	2ksps

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

215	0	0	0	0	0

VC 2 Write Pointer 	25935	VC 2 Write Pointer End	25961

VC 2 Read Pointer 	6500	VC 2 Read Pointer End	6500

Apogee Tracking Contact

IBEX Orbit# 363 APOGEE Post-Sun Maneuver  15 Apr 17

CSS Angle TLM	0.231547	10 Apr 16 @1000 UTC

CSS Sun-Pointing Angle	0.463094

CSS Angle TLM	0.315279	15 Apr 17 @1300 UTC

CSS Sun-Pointing Angle	0.630558

Pre-Burn

Thruster 1	12768	10 Apr 16 @1000 UTC

Thruster 2	12480

Thruster 3	13712

Thruster 4	14000

Post-Burn

Thruster 1	13008	15 Apr 17 @1300 UTC

Thruster 2	12720

Thruster 3	14112

Thruster 4	14400

Number of Pulses

Thruster 1	240

Thruster 2	240

Thruster 3	400

Thruster 4	400

Thruster Pairs

Thruster 1 & 2	480

Thruster 3 & 4	800