IBEX Goat Herder  19 Apr 17

The Perigee contacts for Orbit# 365 were nominal for command telemetry and the inertial maneuver successful

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Wednesday, April 19, 2017	109	0800	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	907	10 desc	40ksps	187 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1688	6	1441	34	0	0

VC 2 Write Pointer 	45253	VC 2 Write Pointer End	45289

VC 2 Read Pointer 	26457	VC 2 Read Pointer End	26457

IBEX Orbit# 363 Tracking Contact

reset_master_timer.scr

@FMI_SetDownlink(64)

CAR# 907 Upload Orbit# 365 ATS 	1.IBEX_2017_118_o0365a_v001.scr (976-73)

ops_set_sc_time.scr

@ACT_ResetTaskRawFailed 	(AC_FDC)

@FMI_SetDownlink(40k)

@FTG_DumpBAckorbit (from start,0,0,0,0)

IBEX Orbit# 363 PERIGEE Tracking Contact  19 Apr 17

J2000	Spin Axis

ECI X	0.894038

ECI Y	0.410196

ECI Z	0.180095

Precession Maneuver

MPS Diff	0.787	deg

MPS Diff should be < 1.5

Right Ascension - RA	24.646	deg

Declination - DEC	10.375	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-2.927	deg

0.42613800	ActNor.EstInrToBdy[0]

0.47786900	ActNor.EstInrToBdy[1]

0.70374500	ActNor.EstInrToBdy[2]

0.30788100	ActNor.EstInrToBdy[3]

1176630000.000	ActNor.EstTime

MPS Generated Target Vectors

MPS Cmd Vector X	0.890695000

MPS Cmd Vector Y	0.420801000

MPS Cmd Vector Z	0.172015000

CSS Angle TLM	0.315279	15 Apr 17 @1300 UTC

CSS Sun-Pointing Angle	0.630558

CSS Angle TLM	0.845341	19 Apr 17 @0800

CSS Sun-Pointing Angle	1.690682

Pre-Burn

Thruster 1	13008	15 Apr 17 @1300 UTC

Thruster 2	12720

Thruster 3	14112

Thruster 4	14400

Post-Burn

Thruster 1	13152	19 Apr 17 @0800

Thruster 2	12864

Thruster 3	14256

Thruster 4	14544

Number of Pulses

Thruster 1	144

Thruster 2	144

Thruster 3	144

Thruster 4	144

Thruster Pairs

Thruster 1 & 2	288

Thruster 3 & 4	288

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Wednesday, April 19, 2017	109	1300	AUWA	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	10 asc	320ksps	244 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1157	1	0	0	18931	0

VC 2 Write Pointer 	45386	VC 2 Write Pointer End	45403

VC 2 Read Pointer 	26457	VC 2 Read Pointer End	45388

Orbit# 363  SSR_Dump/Tracking contact

SSR_Dump.scr (new)

stx_off