IBEX Goat Herder  7 May 17

The Perigee Contacts for Orbit# 365 were nominal for command/telemetry and the inertial maneuver successful.

The SSR pointers were reset to 6500

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Saturday, May 06, 2017	126	2200	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

TPerry	910	12 d	2ksps	169

EBNO Values	EBNO Values 3	AGC Strength

14.33 - 22.55	-110 ->-119 @2k

EBNO Values 2	AGC Strength 2

13.2 - 21.5

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

376	63	0	0	0	0

VC 2 Write Pointer 	0	VC 2 Write Pointer End	0

VC 2 Read Pointer 	0	VC 2 Read Pointer End	0

ATS Upload: IBEX_2017_136_o0367_v001  (99 cmds Trk # 419 – 517)

Reset Master Timer

Q1 -0.45812100

Q2 -0.38918500

Q3 -0.79899600

Q4 0.01626900

GPS sec 1178143815.000

MPS Diff 0.713

MPS Cmd Vector X 0.714991000

MPS Cmd Vector Y 0.645183000

MPS Cmd Vector Z 0.269306000

CSS Angle TLM 1.04343 03 May 17 @1300

CSS Sun-Pointing Angle 2.08686

CSS Angle TLM 0.372729 06 May 17 @2200

CSS Sun-Pointing Angle 0.745458

Pre-Burn

Thruster 1 13984 03 May 17 @1300

Thruster 2 13664

Thruster 3 15104

Thruster 4 15424

Post-Burn

Thruster 1 14272 06 May 17 @2200

Thruster 2 13952

Thruster 3 15408

Thruster 4 15728

Number of Pulses

Thruster 1 288

Thruster 2 288

Thruster 3 304

Thruster 4 304

Thruster Pairs

Thruster 1 & 2 576

Thruster 3 & 4 608

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Sunday, May 07, 2017	127	1000	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	11 asc	320ksps	180 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1862	1	0	0	19056	0

VC 2 Write Pointer 	18150	VC 2 Write Pointer End	6527

VC 2 Read Pointer 	18150	VC 2 Read Pointer End	6500

Orbit# 365  SSR_Dump/Tracking Contact

1.SSR_Dump.scr (new, RESET PNTR 6500)

2. ops_set_sc_time.scr

3. @ACT_ResetTaskRawFAiled (AC_FDC)