IBEX Goat Herder  16 May 17

The Perigee contacts for Orbit# 366 were nominal for command/telemetry and the inertial maneuver successful.

The FC Clock rolled over on doy 134@0007 (14 May 17)

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Monday, May 15, 2017	135	1830	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

TPerry	12 desc	2ksps	180 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

380	56	0	0	0	0

VC 2 Write Pointer 	25306	VC 2 Write Pointer End	25337

VC 2 Read Pointer 	6500	VC 2 Read Pointer End	6500

Orbit# 366 Tracking Contact  reset_master_timer.scr

@FMI_SetDownlink(40k)

@FMI_SetDownlink(2k)

@ACT_TaskRawFailed (AC_FDC)

FC Clock rolled over (doy 134@0007)

IBEX Orbit# 366 PERIGEE Target Vectors  15 May 17

J2000	Spin Axis

ECI X	0.610452

ECI Y	0.726190

ECI Z	0.316221

Precession Maneuver

MPS Diff	0.816	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	49.949	deg

Declination - DEC	18.435	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-2.735	deg

-0.42650800	ActNor.EstInrToBdy[0]

-0.39997500	ActNor.EstInrToBdy[1]

-0.80555400	ActNor.EstInrToBdy[2]

0.09587960	ActNor.EstInrToBdy[3]

1178906441.000	ActNor.EstTime

MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	0.603139000

MPS Cmd Vector Y	0.735581000

MPS Cmd Vector Z	0.308453000

CSS Angle TLM	1.02135	11 May 17 @1500

CSS Sun-Pointing Angle	2.0427

CSS Angle TLM	0.441905	15 May 17 @1830

CSS Sun-Pointing Angle	0.88381

Pre-Burn

Thruster 1	14528	11 May 17 @1500

Thruster 2	14208

Thruster 3	15680

Thruster 4	16000

Post-Burn

Thruster 1	14832	15 May 17 @1830

Thruster 2	14480

Thruster 3	15986

Thruster 4	16320

Number of Pulses

Thruster 1	304

Thruster 2	272

Thruster 3	306

Thruster 4	320

Thruster Pairs

Thruster 1 & 2	576

Thruster 3 & 4	626

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Tuesday, May 16, 2017	136	0700	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	911	11 asc	320ksps	188 watts

EBNO Values	EBNO Values 3	AGC Strength

@0659=4.79-6.72db(320k)	@0659=-106.67db(320k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1192	1	1294	0	19115	0

VC 2 Write Pointer 	25613	VC 2 Write Pointer End	25642

VC 2 Read Pointer 	6500	VC 2 Read Pointer End	25615

Orbit# 366 SSR_Dump/Tracking Contact

CAR#911 Upload Orbit# 368 ATS 1.IBEX_2017_144_o0368a_v002.scr (617-715)

SSR_Dump.scr (new)

ops_set_sc_time.scr

@FTG_DumpBackorbit (from start,0,0,0,0)

stx,off