IBEX Goat Herder  3 Jun 17

The Perigee Contacts for Orbit# 360 were nominal for command/telemetry and the inertial maneuver successful.

The ACE uptime counter rolled over on 1 Jun 17@2047, before the inertial maneuver executed.

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Thursday, June 01, 2017	152	1730	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	913	26 desc	40ksps	180 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

827	0	0	0	0	0

VC 2 Write Pointer 	63883	VC 2 Write Pointer End	63971

VC 2 Read Pointer 	45704	VC 2 Read Pointer End	45704

Orbit# 368 Tracking Contact

Blind_acq.scr (40k)

stx,off(2017:06:01:18:32:00,997)

@FCH_DelTimedCMD (702,stx_on  06:02:18:58:00)

@FCH_DelTimedCMD (707,SSR_Dump 06:02:19:10:00)

CAR# 913 Upload Orbit# 370 ATS  1.IBEX_2017_162_o0370a_v001.scr (998-95)

stx,off

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Saturday, June 03, 2017	154	0500	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius 	S-Band Rate	Station PWR

SWesley	12 asc	160ksps	200 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err	VC 2	VC 2 Seq Err

1906	1	0	0	20802	0

VC 2 Write Pointer 	968	VC 2 Write Pointer End	997

VC 2 Read Pointer 	45704	VC 2 Read Pointer End	970

Orbit# 368 SSR_Dump/Tracking Contact

reset_master_timer.scr

SSR_Dump.scr(new)

ops_set_sc_time

ACE uptime has rolled over on 1Jun17@2047 UTC

IBEX Orbit# 368 PERIGEE Target Vectors 3 Jun 17

J2000	Spin Axis

ECI X	0.347707

ECI Y	0.860491

ECI Z	0.372365

Precession Maneuver

MPS Diff	0.691	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	67.997	deg

Declination - DEC	21.862	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.178	deg

-0.55791800	ActNor.EstInrToBdy[0]

-0.05045130	ActNor.EstInrToBdy[1]

-0.37825300	ActNor.EstInrToBdy[2]

0.73695800	ActNor.EstInrToBdy[3]

1180500000.000	ActNor.EstTime

MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	0.340091000

MPS Cmd Vector Y	0.866562000

MPS Cmd Vector Z	0.365251000

| CSS Angle TLM | 4.07429 | 1 Jun 17 @1730 |
| --- | --- | --- |
| CSS Sun-Pointing Angle | 8.14858 |  |
| CSS Angle TLM | 0.71737 | 3 Jun 17 @0500 |
| CSS Sun-Pointing Angle | 1.43474 |  |
| Pre-Burn |  |  |
| Thruster 1 | 15632 | 1 Jun 17 @1730 |
| Thruster 2 | 15280 |  |
| Thruster 3 | 16832 |  |
| Thruster 4 | 17184 |  |
| Post-Burn |  |  |
| Thruster 1 | 288 | 3 Jun 17 @0500 |
| Thruster 2 | 288 |  |
| Thruster 3 | 272 |  |
| Thruster 4 | 272 |  |
| Number of Pulses |  |  |
| Thruster 1 | 288 |  |
| Thruster 2 | 288 |  |
| Thruster 3 | 272 |  |
| Thruster 4 | 272 |  |
| Thruster Pairs |  |  |
| Thruster 1 & 2 | 576 |  |
| Thruster 3 & 4 | 544 |  |