IBEX Goat Herder  21 June 17

The Perigee contacts for Orbit# 370 were nominal for command/telemetry and the inertial maneuver successful

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Tuesday, June 20, 2017	171	1800	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

TPerry	916	64ksps	180

EBNO Values	EBNO Values 3	AGC Strength

6.11 -> 8.28	-106

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1901	1	0	0	0	0

VC 2 Write Pointer Start	0	VC 2 Write Pointer End	0

VC 2 Read Pointer Start	0	VC 2 Read Pointer End	0

ATS upload - IBEX_181_o0372a_v003 95 cmds

Trk # 370 - 464 & 465

1 CMD had to be retransmitted

Reset FDC Totals

Reset master Timer

Maneuver was nominal

Q1 -0.39622300 ActNor.EstInrToBdy[0]

Q2 0.37840900 ActNor.EstInrToBdy[1]

Q3 0.54103700 ActNor.EstInrToBdy[2]

Q4 0.63803800 ActNor.EstInrToBdy[3]

GPS sec 1182016851.000 ActNor.EstTime

MPS Diff 0.756

MPS Cmd Vector X 0.049157000

MPS Cmd Vector Y 0.920145000

MPS Cmd Vector Z 0.388481000

CSS Angle TLM 1.13729 17 Jun 17@1100

CSS Sun-Pointing Angle 2.27458

0.550008 20 Jun 17 @1800

CSS Sun-Pointing Angle 1.100016

Pre-Burn

Thruster 1 1120 17 Jun 17@1100

Thruster 2 1088

Thruster 3 1136

Thruster 4 1168

Post-Burn

Thruster 1 1392 20 Jun 17 @1800

Thruster 2 1360

Thruster 3 1408

Thruster 4 1440

Number of Pulses

Thruster 1 272

Thruster 2 272

Thruster 3 272

Thruster 4 272

Thruster Pairs

Thruster 1 & 2 544

Thruster 3 & 4 544

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Wednesday, June 21, 2017	172	0400	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	13 asc	160ksps	200 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1908	1	0	0	21376	0

VC 2 Write Pointer Start	27875	VC 2 Write Pointer End	27904

VC 2 Read Pointer Start	6500	VC 2 Read Pointer End	27876

Orbit# 370 Perigee SSR_Dump/Tracking Contact

SSR_Dump.scr (new)

ops_set_sc_time.scr