IBEX Goat Herder 25 Jun 17

The Apogee contact for Orbit# 371 was nominal for command/telemetry and the inertial maneuver successful.

The Apogee contact was taken on the MAESTRO03 server and CMD3.

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Sunday, June 25, 2017	176	1100	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	Apogee	2ksps	180 watts

EBNO Values	EBNO Values 3	AGC Strength

@1100=12/50-16.00db (2k)	@1100=-113.40db(2k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

213	2	0	0	0	0

VC 2 Write Pointer Start	37008	VC 2 Write Pointer End	37072

VC 2 Read Pointer Start	27876	VC 2 Read Pointer End	27876

Orbit# 371 Apogee Tracking Contact

@FMI_SetDownlink (40k)

@FMI_SetDownlink(2k)

IBEX Orbit# 371 APOGEE Target Vectors  25 Jun 17

J2000	Spin Axis

ECI X	-0.020035

ECI Y	0.916074

ECI Z	0.400509

Precession Maneuver

MPS Diff	0.843	deg

*MPS Diff should be < 1.5*

-0.31014000	ActNor.EstInrToBdy[0]

0.45117500	ActNor.EstInrToBdy[1]

0.69979900	ActNor.EstInrToBdy[2]

0.45884200	ActNor.EstInrToBdy[3]

1182430000.000	ActNor.EstTime

Right Ascension - RA	91.253	deg

Declination - DEC	23.610	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.020	deg

MPS Generated APOGEE Target Vectors

MPS Cmd Vector X	-0.026022000

MPS Cmd Vector Y	0.921245000

MPS Cmd Vector Z	0.388111000

CSS Angle TLM	0.5550008	20 Jun 17 @1800

CSS Sun-Pointing Angle	1.1100016

0.605226	25 Jun 17 @1100

CSS Sun-Pointing Angle	1.210452

Pre-Burn

Thruster 1	1392	20 Jun 17 @1800

Thruster 2	1360

Thruster 3	1408

Thruster 4	1440

Post-Burn

Thruster 1	1664	25 Jun 17 @1100

Thruster 2	1632

Thruster 3	1696

Thruster 4	1728

Number of Pulses

Thruster 1	272

Thruster 2	272

Thruster 3	288

Thruster 4	288

Thruster Pairs

Thruster 1 & 2	544

Thruster 3 & 4	576