IBEX Goat Herder  9 July 17

The Perigee contacts for Orbit# 372 were nominal for command/telemetry and the  maneuver successful.

The SSR pointers were reset to 6500.

VC2= 20715 with 0 errors

The star tracker power cycled on 9 July 17 @09:59:45  and the AC_FDC latches/totals were reset

The following objectives were accomplished

- reset_master_timer.scr

- SSR_Dump.scr (new,reset_pntrs,6500)

- CAR# 919 Upload Orbit# 374 ATS

IBEX_2017_199_o0374a_v001.scr (147-234)

- @FMI_SetDownlink (2k)

- Start Tracker Power Cycled

  - Standing CAR# 344 Reset FDC Totals and Response Latch Totals

  - S924-OP31210 Reset ACE FDC Latch Operating Procedure

    - ACT_ResetRespReqLatch(AC_FDC,FDC_STA,FDC_STA_STALETEST

    - ACT_ResetRespReqLatch(AC_FDC,FDC_STA,FDC_STA_NOSOLUTIONTEST)

  - S924-OP31211 Reset ACS FDC Totals

    - ACT_ResetTaskRawFailed (AC_FDC)

| CSS Angle TLM | 2.77594 |  |
| --- | --- | --- |
| CSS Sun-Pointing Angle | 5.55188 |  |
|  |  | 5 July 17 @1300 |
| CSS Angle TLM | 0.223812 |  |
| CSS Sun-Pointing Angle | 0.447624 |  |
|  |  | 8 July 17 @2230 |
| Pre-Burn |  |  |
| Thruster 1 | 2256 | 5 July 17 @1300 |
| Thruster 2 | 2192 |  |
| Thruster 3 | 2272 |  |
| Thruster 4 | 2336 |  |
| Post-Burn |  |  |
| Thruster 1 | 2560 | 8 July 17 @2230 |
| Thruster 2 | 2496 |  |
| Thruster 3 | 2720 |  |
| Thruster 4 | 2784 |  |
| Number of Pulses |  |  |
| Thruster 1 | 304 |  |
| Thruster 2 | 304 |  |
| Thruster 3 | 448 |  |
| Thruster 4 | 448 |  |
| Thruster Pairs |  |  |
| Thruster 1 & 2 | 608 |  |
| Thruster 3 & 4 | 896 |  |