IBEX Goat Herder  18 Jul 17

The perigee contacts for Orbit# 373 were nominal for command/telemetry and the inertial maneuver successful.

The Pre-Eclipse ATS commands for Orbit# 375 were uploaded (331-426)

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Monday, July 17, 2017	198	2345	AUWA	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	10 asc	160ksps	241 watts

EBNO Values	EBNO Values 3	AGC Strength

@2345=5.89-7.48db(160k)	@2345=-102.32db(160k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1912	1	0	0	21032	0

VC 2 Write Pointer Start	27529	VC 2 Write Pointer End	27560

VC 2 Read Pointer Start	6500	VC 2 Read Pointer End	27532

Orbit# 373 SSR_Dump/Tracking Contact

reset_master_timer.scr

SSR_Dump.scr (new)

IBEX Orbit# 373 PERIGEE Target Vectors 17 Jul 17 @2345

CSS Angle TLM	2.56926

CSS Sun-Pointing Angle	5.13852

14 Jul 17 @1336

CSS Angle TLM	0.454565

CSS Sun-Pointing Angle	0.90913

17 Jul 17 @2345

Pre-Burn

Thruster 1	2736	14 Jul 17 @1336

Thruster 2	2672

Thruster 3	2912

Thruster 4	2976

Post-Burn

Thruster 1	3040	17 Jul 17 @2345

Thruster 2	2944

Thruster 3	3184

Thruster 4	3280

Number of Pulses

Thruster 1	304

Thruster 2	272

Thruster 3	272

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	576

Thruster 3 & 4	576

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Tuesday, July 18, 2017	199	0330	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	920	10 asc	320ksps

EBNO Values	EBNO Values 3	AGC Strength

@0330=7.34-8.20db(320k)	@0330=-101.34db(320k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

962	1	1293	0	0	0

VC 2 Write Pointer Start	27626	VC 2 Write Pointer End	27648

VC 2 Read Pointer Start	27532	VC 2 Read Pointer End	27532

Orbit# 373 Tracking Contact/CAR# 920 Upload Orbit# 375 Pre-Eclipse 1. IBEX_2017_208_o0375a_pre_eclipse_v001.scr (331-426)

@FTG_DumpBackorbit(from start,0,0,0,0)