IBEX Goat Herder  23 July 17

The Apogee Contact for Orbit# 374 were nominal for command/telemetry and the inertial maneuver successful

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Sunday, July 23, 2017	204	1200	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	46 desc	2ksps	179 watts

EBNO Values	EBNO Values 3	AGC Strength

@1200=15.29-17.38db(2k)	@1200=-118.87db(2k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

240	1	0	0	0	0

VC 2 Write Pointer Start	39928	VC 2 Write Pointer End	40003

VC 2 Read Pointer Start	27532	VC 2 Read Pointer End	27532

Orbit# 374 Apogee Tracking Contact

@FMI_SetDownlink(40k)

@FMI_SetDownlink(2k)

IBEX Orbit# 374 APOGEE Target Vectors 23 July 17 @1200

J2000	Spin Axis

ECI X	-0.458547

ECI Y	0.814556

ECI Z	0.355294

Precession Maneuver

MPS Diff	0.741	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	119.377	deg

Declination - DEC	20.811	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.568	deg

-0.53813700	ActNor.EstInrToBdy[0]

0.18100100	ActNor.EstInrToBdy[1]

0.61143600	ActNor.EstInrToBdy[2]

0.55117400	ActNor.EstInrToBdy[3]

1184850000.000	ActNor.EstTime

MPS Generated APOGEE Target Vectors

MPS Cmd Vector X	-0.462095000

MPS Cmd Vector Y	0.817716000

MPS Cmd Vector Z	0.343234000

CSS Angle TLM	0.454565

CSS Sun-Pointing Angle	0.90913

17 Jul 17 @2345

CSS Angle TLM	0.89613

CSS Sun-Pointing Angle	1.79226

23 July 17 @1200

Pre-Burn

Thruster 1	3040	17 Jul 17 @2345

Thruster 2	2944

Thruster 3	3184

Thruster 4	3280

Post-Burn

Thruster 1	3312	23 July 17 @1200

Thruster 2	3216

Thruster 3	3488

Thruster 4	3584

Number of Pulses

Thruster 1	272

Thruster 2	272

Thruster 3	304

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	544

Thruster 3 & 4	608