IBEX Goat Herder  5 Aug 17

The Perigee contacts for Orbit# 375 were nominal for command/telemetry and the inertial maneuver successful.

The FC was dumped and enabled and the SSR_PNTRS reset to 6500.

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Saturday, August 05, 2017	217	0330	AUWA	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	928	13 Desc	64ksps	220 watts

EBNO Values	EBNO Values 3	AGC Strength

@0331=9.20-11.37db(64k)	@0331=-105.112db(64k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

2048	1	1450	35	0	0

VC 2 Write Pointer Start	3259	VC 2 Write Pointer End	3303

VC 2 Read Pointer Start	49039	VC 2 Read Pointer End	49039

Orbit# 375 Perigee Tracking Contact

reset_master_timer.scr

CAR# 928 Upload Orbit# 377 ATS 1.IBEX_2017_226_o0377a_v001.scr(804-900)

@FMI_SetDownlink(40ksps)

@FTG_DumpBAckorbit(from start,0,0,0,0)

@FTV_EnableBoTm

ops_set_sc_time.scr

IBEX Orbit# 375 PERIGEE Target Vectors 5 Aug 17@0330 UTC

J2000	Spin Axis

ECI X	-0.647445

ECI Y	0.699036

ECI Z	0.303586

Precession Maneuver

MPS Diff	0.693	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	132.806	deg

Declination - DEC	17.673	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-2.567	deg

-0.43735300	ActNor.EstInrToBdy[0]

-0.39614300	ActNor.EstInrToBdy[1]

0.00896581	ActNor.EstInrToBdy[2]

0.80728700	ActNor.EstInrToBdy[3]

1185940000.000	ActNor.EstTime

MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	-0.652599000

MPS Cmd Vector Y	0.698897000

MPS Cmd Vector Z	0.292672000

CSS Angle TLM	2.0646

CSS Sun-Pointing Angle	4.1292

3 Aug 17 @1315

CSS Angle TLM	0.370623

CSS Sun-Pointing Angle	0.741246

5 Aug 17 @0330

Pre-Burn

Thruster 1	3856	3 Aug 17 @1315

Thruster 2	3760

Thruster 3	4080

Thruster 4	4176

Post-Burn

Thruster 1	4144	5 Aug 17 @0330

Thruster 2	4016

Thruster 3	4368

Thruster 4	4496

Number of Pulses

Thruster 1	288

Thruster 2	256

Thruster 3	288

Thruster 4	320

Thruster Pairs

Thruster 1 & 2	544

Thruster 3 & 4	608

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Saturday, August 05, 2017	217	1500	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	10 Asc	160ksps	200 watts

EBNO Values	EBNO Values 3	AGC Strength

@1500=6.70-7.50db(160k)	@1500=-108.36db(160k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1914	1	0	0	20050	0

VC 2 Write Pointer Start	3551	VC 2 Write Pointer End	6529

VC 2 Read Pointer Start	49039	VC 2 Read Pointer End	6500

Orbit# 375 SSR_Dump/Tracking Contact

SSR_Dump.scr(new,PNTR_Reset 6500)