IBEX Goat Herder  14 Aug 17

The Perigee Contacts for Orbit# 378 were nominal for command/telemetry and the inertial maneuver successful.

The SSR was dumped successfully through APL-18 and all data files received.  The SOC will identify any missing data blocks.

RAZOR# 628 ACE Reset

The ACE reset on 5 Aug 17 @1702 UTC. The FDCs were re-enabled on 10 Aug 17

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Monday, August 14, 2017	226	1945	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	929	11 Asc	160ksps	169 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1908	1	1293	0	0	0

VC 2 Write Pointer Start	27676	VC 2 Write Pointer End	27714

VC 2 Read Pointer Start	27408	VC 2 Read Pointer End	27408

Orbit# 376 Perigee Tracking Contact

reset_master_timer.scr

CAR# 929 Upload Orbit# 378 ATS 1.IBEX_2017_236_o0378a_v001.scr(999-96)

@FTG_DumpBAckorbit(from start,0,0,0,0)

IBEX Orbit# 376 PERIGEE Target Vectors 14 Aug 17

CSS Angle TLM	0.727124

CSS Sun-Pointing Angle	1.454248

10 Aug 17 @1200

CSS Angle TLM	0.580135

CSS Sun-Pointing Angle	1.16027

14 Aug 17 @1945

Pre-Burn

Thruster 1	272	10 Aug 17 @1200

Thruster 2	272

Thruster 3	288

Thruster 4	288

Post-Burn

Thruster 1	544	14 Aug 17 @1945

Thruster 2	544

Thruster 3	592

Thruster 4	592

Number of Pulses

Thruster 1	272

Thruster 2	272

Thruster 3	304

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	544

Thruster 3 & 4	608