IBEX Goat Herder  24 Aug 17

The Perigee contacts for Orbit# 379 were nominal for command/telemetry and the inertial maneuver successful.

An uncompressed image of the star tracker was dumped.

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Wednesday, August 23, 2017	235	1530	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	928	930	14 desc	160ksps	182 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

2368	0	1288	0	0	0

VC 2 Write Pointer Start	48961	VC 2 Write Pointer End	49066

VC 2 Read Pointer Start	27408	VC 2 Read Pointer End	27408

Orbit# 377 Perigee Tracking Contact/CAR# 928 Star Tracker Image Dump

@AHW_ReadSttlmAttitude

@AKT_ReadAkrTm

@AHW_ReadSttlmHK

@AHW_ReadSttlmFailure

ops_acs_tracker_image.scr (uncompressed)

ops_acs_tracker_check_time.scr

ops_acs_tracker_check_hk.scr

ops_acs_tracker_centroids.scr

ops_acs_tracker_params_dump.scr

@AKT_WriteTlmDest (0,0)

@AHW_ReadSttlmAttitude

@AKT_ReadAkrTm

@AHW_ReadSttlmHK

@AHW_ReadSttlmFailure

reset_master_timer.scr

CAR# 930 Upload Orbit# 379 ATS 	1.IBEX_2017_245_o0379a_v001.scr(190-282)

ops_set_sc_time.scr

@FTG_DumpBAckorbit(from start,0,0,0,0)

IBEX PERIGEE Target Vectors 23 Aug 17

J2000	Spin Axis

ECI X	-0.849984

ECI Y	0.483619

ECI Z	0.208902

Precession Maneuver

MPS Diff	0.569	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	150.361	deg

Declination - DEC	12.058	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-2.493	deg

-0.21825300	ActNor.EstInrToBdy[0]

-0.58984300	ActNor.EstInrToBdy[1]

-0.12608800	ActNor.EstInrToBdy[2]

0.76717200	ActNor.EstInrToBdy[3]

1187540000.000	ActNor.EstTime

MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	-0.852440000

MPS Cmd Vector Y	0.483348000

MPS Cmd Vector Z	0.199300000

CSS Angle TLM	1.16027

CSS Sun-Pointing Angle	2.32054

19 Aug 17 @1000

CSS Angle TLM	0.387654

CSS Sun-Pointing Angle	0.775308

23 Aug 17 @1530

Pre-Burn

Thruster 1	816	19 Aug 17 @1000

Thruster 2	816

Thruster 3	880

Thruster 4	880

Post-Burn

Thruster 1	1120	23 Aug 17 @1530

Thruster 2	1120

Thruster 3	1184

Thruster 4	1184

Number of Pulses

Thruster 1	304

Thruster 2	304

Thruster 3	304

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	608

Thruster 3 & 4	608

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Thursday, August 24, 2017	236	0530	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	11 asc	160ksps	192 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1915	1	0	0	21968	0

VC 2 Write Pointer Start	49375	VC 2 Write Pointer End	49404

VC 2 Read Pointer Start	27408	VC 2 Read Pointer End	49376

Orbit# 377 SSR_Dump/Tracking Contact

SSR_Dump.scr(new)