IBEX Goat Herder  28 Aug 17

The Apogee contact for Orbit# 378 was nominal for command/telemetry and the inertial maneuver was successful

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Monday, August 28, 2017	240	1000	USHI02

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	45 asc	2ksps	135 watts

EBNO Values	EBNO Values 3	AGC Strength

@1003=14.30-16.20db(2k)	@1003=-115.03db(2k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

210	2	0	0	0	0

VC 2 Write Pointer Start	58962	VC 2 Write Pointer End	59016

VC 2 Read Pointer Start	49376	VC 2 Read Pointer End	49376

Orbit# 378 Apogee Tracking Contact

@FMI_SetDownlink (40k)

@FMI_SetDownlink (2k)

IBEX Orbit# 378 APOGEE Target Vectors  28 Aug 17

J2000	Spin Axis

ECI X	-0.888057

ECI Y	0.420912

ECI Z	0.184902

Precession Maneuver

MPS Diff	0.746	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	154.640	deg

Declination - DEC	10.655	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-2.655	deg

-0.63838700	ActNor.EstInrToBdy[0]

0.00336150	ActNor.EstInrToBdy[1]

0.69726400	ActNor.EstInrToBdy[2]

0.32599700	ActNor.EstInrToBdy[3]

1187950000.000	ActNor.EstTime

MPS Generated APOGEE Target Vectors

MPS Cmd Vector X	-0.889670000

MPS Cmd Vector Y	0.422922000

MPS Cmd Vector Z	0.172118000

CSS Angle TLM	0.387654

CSS Sun-Pointing Angle	0.775308

23 Aug 17 @1530

CSS Angle TLM	0.372203

CSS Sun-Pointing Angle	0.744406

28 Aug 17 @1000

Pre-Burn

Thruster 1	1120	23 Aug 17 @1530

Thruster 2	1120

Thruster 3	1184

Thruster 4	1184

Post-Burn

Thruster 1	1456	28 Aug 17 @1000

Thruster 2	1392

Thruster 3	1472

Thruster 4	1536

Number of Pulses

Thruster 1	336

Thruster 2	272

Thruster 3	288

Thruster 4	352

Thruster Pairs

Thruster 1 & 2	608

Thruster 3 & 4	640