IBEX Goat Herder  1 Sept 17

The Perigee Tracking Contact for Orbit# 378 was nominal for command/telemetry and the inertial maneuver successful.

The SSR_Dump will be taken with APL-18 on 2 Sept @1200 UTC

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Friday, September 01, 2017	244	2000	AUWA	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	931	13 desc	160ksps	249 watts

EBNO Values	EBNO Values 3	AGC Strength

@2000=8.16-873db(160k)	@2000=-103.14db(160k)

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1387	0	1286	0	0	0

VC 2 Write Pointer Start	3424	VC 2 Write Pointer End	3456

VC 2 Read Pointer Start	49376	VC 2 Read Pointer End	49376

Orbit# 378 PERIGEE Tracking Contact

reset_master_timer.scr

ops_set_sc_time.scr

@ACT_ResetTaskRawFailed(AC_FDC)

CAR# 931  Upload Orbit# 380 ATS 1.IBEX_2017_254_o0380a_v001.scr(382-480)

@FTG_DumpBackorbit(from start, 0,0,0,0)

stx,off

IBEX Orbit# 380 PERIGEE Target Vectors  1 Sept 17

J2000	Spin Axis

ECI X	-0.920423

ECI Y	0.358241

ECI Z	0.156479

Precession Maneuver

MPS Diff	0.682	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	158.733	deg

Declination - DEC	9.003	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-2.548	deg

-0.46665800	ActNor.EstInrToBdy[0]

-0.45165400	ActNor.EstInrToBdy[1]

0.31738600	ActNor.EstInrToBdy[2]

0.69101800	ActNor.EstInrToBdy[3]

1188330000.000	ActNor.EstTime

MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	-0.922547000

MPS Cmd Vector Y	0.357684000

MPS Cmd Vector Z	0.144805000

CSS Angle TLM	0.372203

CSS Sun-Pointing Angle	0.744406

28 Aug 17 @1000

CSS Angle TLM	0.364232

CSS Sun-Pointing Angle	0.728464

1 Sept 17 @2000

Pre-Burn

Thruster 1	1456	28 Aug 17 @1000

Thruster 2	1392

Thruster 3	1472

Thruster 4	1536

Post-Burn

Thruster 1	1728	1 Sept 17 @2000

Thruster 2	1664

Thruster 3	1760

Thruster 4	1824

Number of Pulses

Thruster 1	272

Thruster 2	272

Thruster 3	288

Thruster 4	288

Thruster Pairs

Thruster 1 & 2	544

Thruster 3 & 4	576