IBEX Goat Herder  16 Sept 17

The Apogee Tracking Contact for Orbit# 380 was nominal for command/telemetry and the inertial maneuver successful.

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

259	0900	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	Apogee	2ksps	175 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

665	5	1435	31	0	0

VC 2 Write Pointer Start	19558	VC 2 Write Pointer End	19640

VC 2 Read Pointer Start	6500	VC 2 Read Pointer End	6500

Orbit# 380 Apogee Tracking Contact

@FMI_SetDownlink (40k)

@FTG_DumpBAckorbit(from start,0,0,0,0)

IBEX Orbit# 380 APOGEE Target Vectors 16 Sept 17

J2000	Spin Axis

ECI X	-0.986138

ECI Y	0.152733

ECI Z	0.064849

Precession Maneuver

MPS Diff	0.562	deg

*MPS Diff should be < 1.5*

Right Ascension - RA	171.196	deg

Declination - DEC	3.718	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.260	deg

-0.41921600	ActNor.EstInrToBdy[0]

-0.54021600	ActNor.EstInrToBdy[1]

0.35384200	ActNor.EstInrToBdy[2]

0.63813800	ActNor.EstInrToBdy[3]

1189590000.000	ActNor.EstTime

MPS Generated APOGEE Target Vectors

MPS Cmd Vector X	-0.986690000

MPS Cmd Vector Y	0.152995000

MPS Cmd Vector Z	0.055090000

CSS Angle TLM	2.53196

CSS Sun-Pointing Angle	5.06392

12 Sept 17 @2231

CSS Angle TLM	0.690972

CSS Sun-Pointing Angle	1.381944

16 Sept 17 @0900

Pre-Burn

Thruster 1	2272	12 Sept 17 @2231

Thruster 2	2208

Thruster 3	2352

Thruster 4	2416

Post-Burn

Thruster 1	2560	16 Sept 17 @0900

Thruster 2	2496

Thruster 3	2656

Thruster 4	2720

Number of Pulses

Thruster 1	288

Thruster 2	288

Thruster 3	304

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	576

Thruster 3 & 4	608