IBEX Goat Herder  21 Sept 17

The PERIGEE contacts for Orbit# 380 were nominal for command/telemetry and the inertial maneuver successful.

The SSR data was dumped through APL-18 and the IBEX_Lo Sweep Table was loaded at the beginning of Orbit# 381 arc a.

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Wednesday, September 20, 	263	2245	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	933	12 asc	64ksps	252 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1693	4	1445	32	0	0

VC 2 Write Pointer Start	28999	VC 2 Write Pointer End	29038

VC 2 Read Pointer Start	28694	VC 2 Read Pointer End	28694

Orbit# 380 Perigee Tracking Contact

reset_master_timer.scr

ops_set_sc_time.scr

CAR#933 Upload Orbit# 382 ATS IBEX_2017_272_o0382a_v001.scr

FMI_SetDownlink(40k)

@FTG_DumpBackorbit(from start,0,0,0,0)

IBEX Orbit# 380 PERIGEE Target Vectors  20 Sept 17

J2000	Spin Axis

ECI X	-0.995926

ECI Y	0.082124

ECI Z	0.037248

Precession Maneuver

MPS Diff	0.760	deg

*MPS Diff should be < 1.5*

0.41040200	ActNor.EstInrToBdy[0]

-0.55941600	ActNor.EstInrToBdy[1]

-0.47226200	ActNor.EstInrToBdy[2]

0.54368400	ActNor.EstInrToBdy[3]

1189990000.000	ActNor.EstTime

Right Ascension - RA	175.286	deg

Declination - DEC	2.135	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.404	deg

MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	-0.996542000

MPS Cmd Vector Y	0.079480000

MPS Cmd Vector Z	0.024240000

CSS Angle TLM	0.690972

CSS Sun-Pointing Angle	1.381944

16 Sept 17 @0900

CSS Angle TLM	0.658194

CSS Sun-Pointing Angle	1.316388

20 Sept 17 @2245

Pre-Burn

Thruster 1	2560	16 Sept 17 @0900

Thruster 2	2496

Thruster 3	2656

Thruster 4	2720

Post-Burn

Thruster 1	2848	16 Sept 17 @0900

Thruster 2	2784

Thruster 3	2960

Thruster 4	3024

Number of Pulses

Thruster 1	288

Thruster 2	288

Thruster 3	304

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	576

Thruster 3 & 4	608

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Thursday, September 21, 2017	264	0415	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	918	15 asc	2ksps	250 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

174	2	0	0	0	0

VC 2 Write Pointer Start	29294	VC 2 Write Pointer End	29334

VC 2 Read Pointer Start	28694	VC 2 Read Pointer End	28694

@FMI_SetDownlink(2k)

Orbit# 381 Upload IBEX_Lo Normal Sweep Table

1.@CEU_Mode(HVENG)

2.@CEU_Mode(HVSTANDBY)

3.sweep_table_uplaod_160922.scr(Table_Lo_12345678_Normal,quit)

4.@CEU_Mode(HVENG) 5. @CEU_Mode(HVSCI)