IBEX Goat Herder  26 Sept 17

The Apogee tracking contact for Orbit# 381 was nominal for command/telemetry and the inertial maneuver successful

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Tuesday, September 26, 2017	269	0900	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	43 desc	2ksps	172 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

666	4	1442	32	0	0

VC 2 Write Pointer Start	42276	VC 2 Write Pointer End	42359

VC 2 Read Pointer Start	28694	VC 2 Read Pointer End	28694

Orbit# 381 Apogee Tracking Contact

@FMI_SetDownlink(40k)

@FTG_DumpBAckorbit(from start,0,0,0,0)

IBEX Orbit# 381 APOGEE Target Vectors 26 Sept 17

J2000	Spin Axis

ECI X	-0.999942

ECI Y	0.010323

ECI Z	0.002926

Precession Maneuver

MPS Diff	0.612	deg

*MPS Diff should be < 1.5*

-0.14449300	ActNor.EstInrToBdy[0]

-0.69112900	ActNor.EstInrToBdy[1]

0.13775300	ActNor.EstInrToBdy[2]

0.69461300	ActNor.EstInrToBdy[3]

1190450000.000	ActNor.EstTime

Right Ascension - RA	179.409	deg

Declination - DEC	0.168	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-4.056	deg

MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	-0.999935000

MPS Cmd Vector Y	0.008482000

MPS Cmd Vector Z 	-0.007557000

CSS Angle TLM	0.658194

CSS Sun-Pointing Angle	1.316388

20 Sept 17 @2245

CSS Angle TLM	1.09367

CSS Sun-Pointing Angle	2.18734

26 Sept 17 @0900

Pre-Burn

Thruster 1	2848	20 Sept 17 @2245

Thruster 2	2784

Thruster 3	2960

Thruster 4	3024

Post-Burn

Thruster 1	3120	26 Sept 17 @0900

Thruster 2	3056

Thruster 3	3264

Thruster 4	3328

Number of Pulses

Thruster 1	272

Thruster 2	272

Thruster 3	304

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	544

Thruster 3 & 4	608