IBEX Goat Herder  30 Sept 17

The Perigee contacts for Orbit# 381 were nominal for command/telemetry and the inertial maneuver successful

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Friday, September 29, 2017	272	1300	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	13 desc	320ksps	170 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1908	0	0	0	21259	0

VC 2 Write Pointer Start	49951	VC 2 Write Pointer End	49980

VC 2 Read Pointer Start	28694	VC 2 Read Pointer End	49953

Orbit# 381 Perigee SSR_Dump/Tracking Contact

reset_master_timer.scr

SSR_Dump.scr (new)

ops_set_sc_time.scr

IBEX Orbit# 381 PERIGEE Target Vectors 29 Sept 17 @1300

J2000	Spin Axis

ECI X	-0.998051

ECI Y	-0.057544

ECI Z	-0.024138

Precession Maneuver

MPS Diff	0.865	deg

*MPS Diff should be < 1.5*

0.52386400	ActNor.EstInrToBdy[0]

-0.48747800	ActNor.EstInrToBdy[1]

-0.48313000	ActNor.EstInrToBdy[2]

0.50449600	ActNor.EstInrToBdy[3]

1190730000.000	ActNor.EstTime

Right Ascension - RA	183.300	deg

Declination - DEC	-1.383	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.051	deg

MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	-0.997249000

MPS Cmd Vector Y	-0.063720000

MPS Cmd Vector Z	-0.037865000

CSS Angle TLM	1.09367

CSS Sun-Pointing Angle	2.18734

26 Sept 17 @0900

CSS Angle TLM	0.455425

CSS Sun-Pointing Angle	0.91085

29 Sept17 @1300

Pre-Burn

Thruster 1	3120	26 Sept 17 @0900

Thruster 2	3056

Thruster 3	3264

Thruster 4	3328

Post-Burn

Thruster 1	3392	29 Sept17 @1300

Thruster 2	3328

Thruster 3	3568

Thruster 4	3632

Number of Pulses

Thruster 1	272

Thruster 2	272

Thruster 3	304

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	544

Thruster 3 & 4	608

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Saturday, September 30, 2017	273	0400	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	13 asc	40ksps	286 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1628	4	1438	33	0	0

VC 2 Write Pointer Start	50316	VC 2 Write Pointer End	50353

VC 2 Read Pointer Start	49953	VC 2 Read Pointer End	49953

Orbit# 381 Perigee Tracking Contact

CAR# 934 Upload ATS 1.IBEX_2017_281_o0383a_v001.scr (956-51)

@FTG_DumpBAckorbit (from start,0,0,0,0)